# Rebuilding a 4948 ROMMon Commands

Below are the ROMMON commands for rebuilding a "dead" Cisco 4948 switch:

- Configure the switch's management port with an available and valid IP address (insure this is not a duplicate IP address), subnet mask and default gateway on a local network that can be accessed at the site. (I used an available user IP address and connected to the existing user rail)

- A TFTP server assignment of 172.16.10.112 also needs to be configured. Here are the commands to set up networking and TFTP on the management port:

  - **********************************************************

  - rommon 1 >set interface fa1

  - rommon 2 >set ip route default

  - rommon 3 >set TftpServer 172.16.10.112

  - **********************************************************

- Connect the 4948's management port to the network. (Treat the management port just like a switch port to determine whether to use a crossover or straight-through cable. (Notification will be given when the management port links up).

- Test your connection by trying to ping 172.16.10.112.

- Once connectivity is verified you can begin the TFTP boot. (TFTP progress will be displayed. The process should take approximately 15 minutes).

- When the transfer is complete, the switch should reboot automatically and as normal. Note: The IOS will not be present on the flash at this time. You will need to copy it as you would normally. Here's the output:

- Established physical link 10MB Half Duplex

- Network layer connectivity may take a few seconds

- rommon 4 >ping 172.16.10.112

- Host 172.16.10.112  is alive

- rommon 5 >boot tftp://cat4000-i5k91s-mz.122-25.EW.bin

- Tftp Session details are ....

- Filename     : /cat4000-i5k91s-mz.122-25.EW.bin

- IP Address   : 10.16.100.10

- TftpServer   : 172.16.10.112