This document is provided without warranty, always vet out what works best for you and your organization.

### HPUX 10.xx  and 11.x Setup 8.xx series (D, E, etc.)

- Insert HP-UX 10.20 Install and Core OS (#56 from CM) into the CD ROM drive.

- Reboot the machine with sync;reboot

- Press any key to interrupt the boot process

- Enter the following:   boot 16/5.2

- Choose N to not interact with IPL.

- Highlight “Install HP-UX”

- Press enter

- Choose Yes to set up Networking

- Press enter

- Hit ctrl-c to stop the DHCP search

- Enter the machine’s hostname (Not the fully qualified hostname.  ““CSI-Internal.com”)

- Enter the IP address of the OUTSIDE interface

- Enter the IP of the Router

- Enter the correct netmask

- This information is NOT temporary, choose no.

- Tab to OK, press return.

- Choose Standard LVM configuration, press return

- Change Primary Swap to 256 (highlight, press return, down arrow, return)

- Tab to OK, press return.

- Tab to Modify FS parameters, press enter.

- Change the configuration to the following parameters.

Note:   This is done by highlighting the appropriate entry, pressing TAB to the “size” entry, deleting the old entry, entering the new value, pressing “TAB” to the modify option and hitting return.

/	-	64 MB

/stand	-	128 MB

(swap)	-	256 MB (this value should already be set)

/home	-	20 MB	(this value should already be set)

/opt	-	252 MB	(this value should already be set)

/tmp	-	64 MB

/usr	-	500 MB

/var	-	remaining free (>400 MB)

- Choose OK, press return

- Choose OK, press return

- Choose Continue, press return

- Wait for all the filesets to be installed (about an hour, depending on the speed of the system.)

- Once they are done, enter y and press return

- enter y and press return again

- Press return

- Enter y and press return yet again

- Choose the proper timezone

- Follow the onscreen directions (yes, they do actually make sense)

- Set the root password (currently using Root as the password)

- Follow the onscreen directions

- Set the IP address information

- Follow the onscreen directions

- Choose Yes for Additional Network Parameters

- Press return

- Enter the Subnet

- Follow the onscreen directions

- Choose Yes for Additional Network Parameters- DNS

Enter the DNS information (rv.tis.com - penn - 10.99.200.51)

- Press return

- Choose NO for NIS

- Choose s for skip font server setup

- Choose y, return

- Return

- Insert the Applications CD as it is rebooting

- Login as root

- Type mount –o cdcase /dev/dsk/c0t2d0 /SD_CDROM

- Type sam

- Press Return

- Choose “Software Management”

- Choose “Install Software to Localhost”

- The Specify source screen will appear, Tab to “OK” and press enter

- Choose OK on the popup screen

- Arrow down to the 100VF-AnyLan/9000 EISA package.  Note: The Multiprocessor HP uses the 100BT EISA drivers.

- Press the spacebar to highlight it.

- Press ALT (which is the F2 key) +A

- Press m for  “mark for install”

- Press enter, and enter again

- Yes should appear in the “Marked” column

- Press ALT (which is the F2 key) +A

- Arrow down to Install (analysis) and press enter.

- Select OK, press enter

- Select Yes and Yes again.

- The “done” option will be available when the install is complete.  Select Done and press return.

- Select OK and press return.

- The system should auto reboot at this time

- Login as root

- Type lanscan

- You should see all of your installed interfaces.  If you do not, it’s because the incorrect package was installed.  Please do steps 47 to 67 again with the correct package.

- Congratulations, you must now configure your nic.  DO NOT USE the ifconfig command.

- Type sam, press return

- Press return

- Choose Networking and Communications

- Press enter

- Choose Network Interface Cards

- Press enter

- Choose your inside interface (it should not be configured)

- Press ALT (which is the F2 key) +A

- Choose Configure

- Enter the IP address, the alias (eg, griffey-internal.rv.tis.com), and the netmask for the interface.

- Choose OK

- The configuration should appear on the screen

- Press F8 (exit)

- Press F8 (exit) again

- Use the ifconfig command to make sure the interface is up.

- Almost there…Stay on Target

- Insert the EXT SW (Extension Software) Disk in the CD-ROM

- Type sam and press return

- Press Return

- Choose Disks and Filesystems

- Choose Disk Devices

- Highlight the CD-ROM using the spacebar

- Press ALT (which is the F2 key) +A

- Choose Add

- Choose Not Using the Logical Volume Manager

- Press return

- Type /SD_CDROM for the “mount directory”

- Un-check the “At every system boot” box

- Choose ‘OK”

- Press enter

- When it is done mounting, press F8

- Arrow up to “..go up”

- Press enter

- Choose Software Management

- Press Enter

- Arrow down to Install Software to Localhost

- Press Enter

- The Specify source screen will appear, Tab to the line that has /SD_CDROM in it.

- Change it to say /SD_CDROM/XSW800GR1020

- Tab to “OK” and press enter

- When the contents are displayed, highlight it (using the spacebar)

- Press F2 (alt) + a

- Press m (for mark for install)

- It should now say Yes in the Marked? Column.

- Press F2 (alt) + a

- Press I (for install)

- Choose OK

- Choose Yes

- Choose Yes

- Tab to “Done” when it becomes available.

- Press return

- Choose OK

- Choose OK again

It should now auto-reboot.

You are now finished, unless you have multiple interfaces.  If so, please repeat steps 72 to 86 to set up any other interfaces BEFORE installing Root.

### HPUX 10.xx  and 11.x Setup 700 series (B132’s, etc)

- Insert HP-UX 10.20 Install and Core OS (#176 from CM) into the CD ROM drive.

- Reboot the machine with sync;reboot

- Press any key to interrupt the boot process

- Enter the following:   sea

- Enter the following:	boot P0

- Choose N to not interact with IPL.

- Enter 45 (for US english)

- Press return and return again

- Highlight “Install HP-UX”

- Press enter

- Choose Yes to set up Networking

- Press enter

- Hit ctrl-c to stop the DHCP search

- Enter the machine’s hostname (Not the fully qualified hostname.  ““CSI-Internal.com”)

- Enter the IP address of the OUTSIDE interface

- Enter the IP of the Router

- Enter the correct netmask

- This information is NOT temporary, choose no.

- Tab to OK, press return.

- Choose Standard LVM configuration, press return

- Change Primary Swap to 256 (highlight, press return, down arrow, return)

- Tab to OK, press return.

- Tab to Modify FS parameters, press enter.

- Change the configuration to the following parameters.

Note:   This is done by highlighting the appropriate entry, pressing TAB to the “size” entry, deleting the old entry, entering the new value, pressing “TAB” to the modify option and hitting return.

/	-	64 MB

/stand	-	128 MB

(swap)	-	256 MB (this value should already be set)

/home	-	20 MB	(this value should already be set)

/opt	-	252 MB	(this value should already be set)

/tmp	-	64 MB

/usr	-	500 MB

/var	-	remaining free (>400 MB)

Note:  The filesystem can be fudged a little if there is a HUGE amount of disk space (4-8 Gig).  I would recommend upping the swap, stand and root if this is the case.

- Choose OK, press return

- Choose OK, press return

- Choose Continue, press return

- Wait for all the filesets to be installed (about an hour, depending on the speed of the system.) The machine should reboot itself.

- Click Yes

- Click Yes

- Click OK

- Click Yes

- Choose the proper timezone

- Follow the onscreen directions (yes, they do actually make sense)

- Set the root password (currently using Root as the password)

- Follow the onscreen directions

- Set the IP address information

- Follow the onscreen directions

- Choose Yes for Additional Network Parameters

- Enter the Subnet, Gateway and Hostname (NOT fully qualified)

- Choose OK

- Follow the onscreen directions

- Choose Yes for Additional Network Parameters- DNS

- Enter the DNS information (rv.tis.com - penn - 10.99.200.51)

- Click OK then Yes then Close

- Click CANCEL on the NIS screen

- Choose no for font server setup

- Choose close

- Insert the Applications CD as it is rebooting

- Choose Command Line Login from the CDE login screen under Options.

- Login as root

- Type mount –o cdcase /dev/dsk/c12d0 /SD_CDROM

- Type sam

- Press Return until you see the sam screen pop up.  (If it is asking questions about term type, just press return.  The defaults will work fine)

- Choose “Software Management”

- Choose “Install Software to Localhost”

- The Specify source screen will appear, Tab to “OK” and press enter

- Choose OK on the popup screen

- Arrow down to the 100BT PCI drivers.  (They should be package #’s B5509BA and B5511BA)

- Press the spacebar to highlight them.

- Press ALT (which is the F2 key) +A

- Press m for  “mark for install”

- Press enter, and enter again

- Yes should appear in the “Marked” column

- Press ALT (which is the F2 key) +A

- Arrow down to Install (analysis) and press enter.

- Select OK, press enter

- Select Yes and Yes again.

- The “done” option will be available when the install is complete.  Select Done and press return.

- Select OK and press return.

- The system should auto reboot at this time

- Choose Command Line Login from the CDE login screen under Options.

- Login as root

- Type lanscan

- You should see all of your installed interfaces.  If you do not, it’s because the incorrect package was installed.  Please do steps 47 to 67 again with the correct package.

- Congratulations, you must now configure your nic.  DO NOT USE the ifconfig command.

- Type sam, press return

- Press return

- Choose Networking and Communications

- Press enter

- Choose Network Interface Cards

- Press enter

- Choose your inside interface (it should not be configured)

- Press ALT (which is the F2 key) +A

- Choose Configure

- Enter the IP address, the alias (eg, griffey-internal.rv.tis.com), and the netmask for the interface.

- Choose OK

- Choose OK again.

- The configuration should appear on the screen

- Press F8 (exit)

- Press F8 (exit) again

- Use the ifconfig command to make sure the interface is up.

- Almost there…Stay on Target

- Insert the EXT SW (Extension Software) Disk in the CD-ROM

- Type sam and press return

- Press Return

- Choose Disks and Filesystems

- Choose Disk Devices

- Highlight the CD-ROM using the spacebar

- Press ALT (which is the F2 key) +A

- Choose Add

- Choose Not Using the Logical Volume Manager

- Press return

- Type /SD_CDROM for the “mount directory”

- Un-check the “At every system boot” box

- Choose ‘OK”

- Press enter

- When it is done mounting, press F8

- Arrow up to “..go up”

- Press enter

- Choose Software Management

- Press Enter

- Arrow down to Install Software to Localhost

- Press Enter

- The Specify source screen will appear, Tab to the line that has /SD_CDROM in it.

- Change it to say /SD_CDROM/XSW700GR1020

- Tab to “OK” and press enter

- When the contents are displayed, highlight it (using the spacebar)

- Press F2 (alt) + a

- Press m (for mark for install)

- It should now say Yes in the Marked? Column.

- Press F2 (alt) + a

- Press I (for install)

- Choose OK

- Choose Yes

- Choose Yes

- Tab to “Done” when it becomes available.

- Press return

- Choose OK

- Choose OK again

- It should now auto-reboot.