Configuration and Deployment Guide

This document describes the principles, guidelines, and best practices for configuring and deploying OneSign V4.0 as well as for upgrading existing OneSign installations to V4.0. It is intended for:

Prospects and technical pre-sales personnel who need to configure a system for quoting purposes (mostly to know how many appliances are needed):

·	Customers and post-sales technical personnel who need to deploy OneSign V4.0.

·	Customers and support personnel who are upgrading an existing OneSign installation to V4.0

·	Note that this document does not contain step-by-step upgrade instructions - refer to the “Upgrading to OneSign 4.0” Tech Brief before you begin upgrading.

For a quick checklist of potential pitfalls when deploying OneSign 4.0, check chapter 7 - Top 10 items to note.

Distributed architecture introduction

OneSign V4.0 provides an enhanced, distributed architecture of multiple, possibly geographically dispersed appliances that are clustered together for scalability, increased availability, and end-user roaming among multiple sites.

By clustering multiple appliances, OneSign can scale to handle environments with hundreds of thousands of users. A cluster of OneSign appliances, called a OneSign Enterprise, can be deployed across LANs and WANs, possibly covering multiple geographical locations. Clustered appliances synchronize information among themselves to support scalability and availability and provide shared services. Because appliances balance end-user loads among them, even customers with simple deployments of two clustered appliances (for example, those upgrading from OneSign 3.x) should expect to see improved end-user performance at peak periods.

In a multi-site enterprise, users can roam among sites and receive the same single sign-on and authentication services throughout the enterprise. Building on OneSign’s computer policies (that augment and can override user policies), different SSO, strong authentication, and physical access control policies can be specified for different sites. For example, a user might not need to badge in when visiting a remote site in order to gain network access, but might need to authenticate via OTP token instead of fingerprint.

The enhanced architecture also increases availability, business continuance, and disaster recovery capabilities. Appliances in a cluster synchronize their databases so that if one appliance fails, the other appliances cover for it and handle its load. If no other appliances in a site are available, appliances in other sites can serve users from the failed site (provided an appropriate underlying network capability). This can be controlled by configuration, to designate specific fail-over sites.

For fault tolerance within a site, this enables a simple N+1 scheme, so that if N appliances are needed to handle a given load, the configuration can accommodate a failure of one appliance with no interruption or degradation of service, or multiple failures with some degradation. Of course, more appliances in the site or in other sites can provide even higher levels of availability, with no degradation of service at all.

Appliances in multiple sites can provide fault tolerance by serving as backup to one another. User enrollments, policies and SSO services are constantly synchronized among sites. If all appliances in a site are inaccessible, OneSign Agents can communicate with appliances in other sites (as configured by the administrator) and the switchover will occur automatically. Alternatively, if the entire site is down, users can “roam” to another site (either physically or via remote access) and be served by appliances in the new site.

Terms and concepts

OneSign Enterprise

A OneSign Enterprise is a cluster of OneSign appliances that synchronize their databases and are configured to work together to service a collection of end-user computers. All appliances in an enterprise share the same users, policies, and enrollments. However, an enterprise can be divided into sites for operational and administrative reasons, mostly to match data center and network topologies. OneSign administrators can also be limited in scope to certain users or sites.

OneSign appliances should be clustered as an enterprise to provide redundancy for business continuity and disaster recovery, and to allow users to roam among multiple sites. However, because of the synchronization overhead involved, you should not define an enterprise only for

the purpose of aggregating reports or consolidating administration tasks. An enterprise is created when the first appliance is configured. Subsequent configured appliances are then added to the enterprise one by one and synchronize with an existing appliance.

OneSign Site

A OneSign site is part of a OneSign enterprise that is defined by the IP address ranges of the computers the site serves and by those appliances in an enterprise that are assigned to the site.

Computers with IP addresses within the site’s IP addresses ranges are considered to belong to that site, referred to as their “home” site. Normally, OneSign agents on these computers will connect to appliances of that site. However, OneSign agents can failover to connect to appliances in other sites in case local appliances are unreachable (this is controllable by the OneSign administrator).

A site that is dedicated to disaster recovery can be designated as a hot standby site, in which case its IP address range is empty. No agents will consider this site as their home site, but if this site is specified as a failover site for another production site, agents will failover to appliances in this site as needed.

Sites are created and appliances are assigned to sites each time an appliance is added to the enterprise (during the wizard process). Each new appliance can be added to an existing site or assigned to a new site. For security, in order to add an appliance to the enterprise, the new appliance must be “invited” by one of the existing appliances, referred to as the “Authorizing Appliance”. In general, any appliance in the enterprise can act as an Authorizing Appliance, and a different one can be used each time. Appliances should be added one at a time. The new appliance synchronizes its database with the Authorizing Appliance. Depending on the size of the database, this can create some network traffic so it is recommended that the Authorizing Appliance be on the same LAN as the new appliance. However, if the new appliance is to be designated as an audit server (see description below) then the Authorizing Appliance must be an audit server too (unless there are no audit servers in the enterprise).

Audit Server

Audit records of end-user activity are kept by OneSign on appliances specially designated as Audit Servers. All audit data is forwarded from a OneSign agent to the appliance with which it is communicating and that appliance propagates that data to all the Audit Servers in the enterprise. Audit servers consume more network bandwidth and so redundancy and performance should be balanced – Imprivata recommends having at least two Audit Servers in a OneSign enterprise, preferably in different sites.

Data Replication

OneSign leverages Oracle technology to replicate information and synchronize among all appliances in an enterprise. Replication scheme is all-to-all, that is, every appliance replicates to all other appliances. Information about users, profiles, policies, and enrollments are synchronized among all appliances. To optimize network traffic, some other data is replicated only within a subset of appliances:

·	End-user sessions are replicated only between appliances within the same site. This is meant to reduce traffic between sites, which often goes over wide area networks

·	Audit information is sent only to Audit Server appliances, again in order to reduce overall network traffic.

When a new appliance is added to the enterprise, it synchronizes its database from an existing appliance.

Information needed prior to configuration

This section describes information that is needed prior to configuring a OneSign enterprise. A preliminary, high-level configuration is needed in pre-sales situations to provide a quote to the prospect. At this stage, it should be enough to determine the number of appliances needed and their division into sites. In most cases, the information that will determine that includes:

·	The number of users, and their locations.

·	Location of data centers that might be involved in servicing those users. Note especially DR

locations and those with terminal servers (Citrix or Windows).

·	Bandwidth and latency between data centers (no need for exact numbers here).

·	Location of domain controllers (this is not mandatory, but might suggest where you could locate OneSign appliances).

For more detailed or complex configurations, and before actual deployment, you should also find out:

·	Overall network topology (mostly to verify connectivity among appliances).

·	IP ranges of clients for each site, including routing tables for remote (VPN) users .

·	Requirements for delegating administration of end-user computers.

·	Location of ID token servers.

·	Location of physical access control servers.

·	Location of networked storage for backup and audit archiving. The next two sections go into details on how to configure OneSign sites and appliances within them, based on the collected information listed above.

Configuring sites

A OneSign site is defined by the IP address ranges of the end-user computers the site serves and by those appliances that are in the site serving these computers. To get a good base for deciding which OneSign sites are needed, look at your network topology and your physical data centers. Appliances in a site typically serve end-user computers that are located in a geographical area served by a data center. However, there are other considerations that might impact the definition of OneSign sites, covered in this section.

User location and network topology

End users expect quick response times for network logins. Therefore, appliances need to be located where they can provide sufficient response time for login access validation. If some users are in a remote site that is connected to the corporate network only through a WAN, you might want to consider creating a OneSign site for those users and placing one or more appliances on the local network.

However, if you have groups of users in different buildings within a campus that are served by a high speed LAN, you need not define multiple OneSign sites and dedicate appliances to serve each building or group of users.

Note that client computer IP ranges defining sites cannot overlap – each site covers a unique range, or ranges, of IP addresses.

External servers

OneSign connects to various external servers such as domain controllers and ID token servers (e.g. SecurID ACE server), as well as physical access control servers (see next section for more details on these). You can assign specific external servers to any OneSign site, overriding the overall enterprise setting. If you want to point different OneSign appliances to unique external servers, you would need to define separate sites. For example, if you have one domain controller in London and one in New York, you could create two OneSign sites and point each one to the relevant domain controller.

Physical access control (PAC) system configuration

You define physical access connectors within OneSign to interface with your PAC systems. The

way you configured your PAC system will impact how OneSign connects to it and potentially also what OneSign sites you should define. For each individual PAC system you should define a physical access connector. The PAC system might have multiple servers, panels, and controllers, but as long as it has one user database, you should define only one connector. Within a connector, you can specify multiple connection configurations to point to multiple PAC servers of that PAC system, if applicable. For example, if you have one PAC system with regional servers in New York and Boston, you might have appliances in New York connect to the regional PAC server in New York, and those in Boston connect to the regional PAC server in Boston.

Defining OneSign sites to compartmentalize appliances and PAC servers in this way can optimize network traffic for verification of login attempts, and is important especially if not all PAC servers are reachable by all OneSign appliances.

This is also important in order to facilitate user network access in various corporate locations that use different PAC systems. If a user is unknown to the PAC system in a given location (e.g., the user travels abroad and visits the company’s local office), having that location’s computers in a separate OneSign site could enable the user to login even if their policy requires badging into the building (which the user cannot do in that remote location). When setting security policies, the OneSign administrator can waive the badge-in requirement for visitors (users that are not mapped to any PAC system in a given site).

Administration delegation

OneSign administrators can be limited in the scope of what end-users computers they can manage by assigning them to specific site(s). For example, a customer might have all end-users in multiple locations on one LAN, so potentially all end-users could be served by one OneSign site, but still prefer to define multiple OneSign sites in order to limit administration privileges by site. Note that scoping administrator roles by site relates to the end-user computers those

administrators can manage, not to the end-users they can manage. End-user scoping is related to domains and OU’s (organizational units) and is unrelated to OneSign sites.

Configuring OneSign appliances among sites

Once a determination was made on the number and location of OneSign sites, you will need to determine how many appliances to place in each site. This section covers considerations for configuring appliances among sites.

Base rules for appliances in enterprise and sites Each OneSign enterprise must contain at least two appliances, for redundancy purposes. While enterprises can function with one appliance, such as in the case of a failure, when first creating the enterprise, or with a test appliance, such configurations should be treated as temporary.

After the first two, appliances can be added as needed. All appliances synchronize one database among them. Each OneSign site must contain at least one appliance. However, there are advantages to having more than one appliance per site, because users will be re-challenged when failing over to work against an appliance in another site (see the Availability section for more details).

Performance considerations

As a rule of thumb, one appliance can typically handle 25,000 – 40,000 users. The exact number depends mostly on the number of concurrent user authentications. If only OneSign Authentication Manager is installed, you should plan for about 1,500 concurrent authentication requests per minute, per appliance. For example, if you anticipate up to 2,500 users logging in concurrently, you should deploy 2 appliances to serve these users. However, if you anticipate more than 3,000 concurrent authentication requests (per minute), you should consult with Imprivata Product Management for a more precise evaluation. If OneSign Single Sign-On is also enabled, plan on 1,000-1,200 authentication requests per minute. Similarly, if OneSign Physical/Logical is enabled, fewer authentication requests per minute can be handled. The number ranges between 500 and 1,500 for one appliance, depending on the specific physical access control system used. For detailed information, please contact Imprivata Product Management.

Audit servers

An appliance can be designated as an audit server when it is added to the enterprise. All OneSign end-user activity is kept in an audit database for reporting purposes. Once an appliance is part of an enterprise, it cannot easily change from an audit server to a non-audit server or vice versa (you will need to remove the appliance form the enterprise, restage it, and add it back). Therefore, you should plan carefully ahead of time which appliances should be designated as audit servers. There should always be at least two audit servers in an enterprise. Backup and restore operations can only be performed on an audit server appliance, so running an enterprise with only one audit server presents a single point of failure from which recovery is much more difficult.

OneSign selects one of the audit server appliances in the enterprise to export scheduled reports and to perform scheduled exports of audit data to FTP servers. Therefore you should verify that each audit server appliance has connectivity to the designated FTP servers for both tasks, preferably on the same LAN. It is recommended that you determine what FTP servers to use after the OneSign enterprise configuration is complete and you see what audit server OneSign chose for these export tasks.

For greater redundancy, you should spread audit servers among multiple sites. However, take into consideration the increased network traffic to audit servers (see the Network Bandwidth section below). For this reason you should also limit the number of audit servers to two or three and avoid designating all appliances in an enterprise as audit servers.

A new appliance can be designated as an audit server when joining the enterprise only if the Authorizing Appliance is an audit server itself, unless there are currently no audit servers in the

enterprise. This is because the new appliance needs to synchronize audit data with the 
authorizing appliance.

Availability considerations

Availability requirements have a significant impact on the number of appliances to configure in each site. Locally within each site, you might want to consider configuring more appliances than are needed to serve end-user computers in that site in order to accommodate for an appliance failure with no interruption or degradation of service. End-user sessions are replicated among the appliances within a site so that if an appliance fails the OneSign Agents on the affected end-user computers and Citrix servers migrate seamlessly to another appliance in the site. Users will not be required to log back into OneSign. Appliances in multiple sites can provide fault tolerance by serving as backup to one another.

User enrollments, policies and SSO services are constantly synchronized among sites. If all appliances in a site are inaccessible, OneSign Agents can communicate with appliances in other sites (as configured by the administrator) and the switchover will occur automatically, though will require users to re-authenticate to OneSign. When planning for failover capacity, remember to allocate enough appliances in each failover site to provide acceptable levels of service for both original and failed-over users.

Network considerations

All appliances in the enterprise synchronize their databases with user, policy, enrollment, and

credential information. Any change in this information on one appliance will be replicated to all other appliances. However, most of the traffic among appliances is generated for user logins. Different amounts of traffic are generated between appliances within a site (typically over a

LAN) and between sites (typically over a WAN).

Between sites, each user login to an appliance generates 4.6 Kbytes of outbound traffic to each other appliance. For example, if there are 4appliances in the enterprise, each in its own site, each login serviced by one of them will generate a total 3*4.6 = 13.8 KB of traffic on the network (this excludes the traffic between the agent and the servicing appliance – see below).

Appliances within a site also replicate user sessions. This adds 6 Kbytes of traffic to the communication among appliances. Therefore, each user login to an appliance generates 10.6 Kbytes of outbound traffic to each other appliance in the same site. For example, if there are 4 appliances in the enterprise, all within the same site, each login serviced by one of them will generate a total 3*10.6 = 31.8 KB of traffic on the network (this excludes the traffic between the agent and the servicing appliance – see below).

In addition, OneSign agents communicate periodically (every 10 minutes by default) with a OneSign server to check status, download any updates, and upload any accumulated audit data (for user activity).

Audit data is propagated first to the server serving that agent and then directly to all audit servers (regardless of whether the serving appliance is an audit server itself or not).

The basic agent-server communication, with no audit data, is on the order of 4 Kbytes per ping (roundtrip). Updated SSO application profiles that need to be downloaded by the agent could add 2-7 Kbytes (roundtrip), depending on the number of application profiles (these numbers are for a range of 20-100). Note that application profiles do not change very frequently, so this should not have a large impact. Audit data adds 20-25 Kbytes to a ping (roundtrip). This data is then replicated from the appliance to all other audit servers in the enterprise.

Currently, OneSign appliances communicate with each other by their real IP addresses only and set up firewall rules accordingly – there is no NAT support. Appliances use port 1521 for replication.

External servers

OneSign selects one of the appliances in the enterprise to perform scheduled synchronization with user directories. Therefore you should verify that each appliance has connectivity to at least one domain controller for each user directory, preferably on the same LAN. In addition, for each physical access connector, OneSign selects one appliance in the sites with which this connector is associated to perform scheduled user mapping with the PAC system.

Keep in mind that when failing over to another site, OneSign appliances in the failover site need to be able to connect to the relevant external servers, such as domain controllers, ID token servers, PAC servers. This is especially important if there is only one appliance in the production site, since any failure would mean that users will work against appliances in another site.

Upgrade considerations

This section describes upgrade considerations for customers who have existing OneSign 3.x deployments and are about to upgrade to V4.0. As with any upgrade, it is recommended that you test your applications in a test environment prior to upgrading your production environment.

OneSign 4.0 uses a new database and so the upgrade from V3.x takes longer than a regular OneSign upgrade. In addition, because of the enhanced architecture of V4.0, you do not need to remain in a primary-failover pair configuration. Instead, you can have two load-sharing appliances, and can also locate them in two separate locations for better redundancy. This is explained in more details further below in this section.

Pre-requirements

Licensing

OneSign 4.0 requires a new license file. You will need to contact Imprivata support to obtain this new license. A license file with all the features and the serial numbers for all the appliances you have purchased will be loaded once during the upgrade process.

Software

You can upgrade to OneSign V4.0 from OneSign V3.0 or later. Customers running Touchpass

3.x will need to upgrade to OneSign 3.x first, and then to OneSign 4.0.

Hardware

2GB of memory is needed in an appliance to run the V4.0 server. Some older appliances do not have enough memory and can be identified in the following ways:

·	The Imprivata name and logo are shown on the upper left of the front panel (see figure 1

below).

·	The serial number on the back starts with 0030485XXXXX.

Figure 1: Older appliance that requires a memory upgrade

Please contact Imprivata support for instructions on how to upgrade your appliances with more memory.

Upgrade from a 3.x primary-failover pair

Customers who have two OneSign 3.x appliances need to decide whether they want to keep the two in the same location or move one to improve business continuity. For example, one appliance can now be moved to another room or floor in the data center, or to another building in the campus. In most cases, when both locations are on the same local area network, it is recommended that both appliances be defined in the same OneSign site. This provides more seamless redundancy because users failing over to another appliance within the same site do not have to re-authenticate. This also provides better end-user performance as both appliances

are active and serving users. However, if desired, one of the appliances can be designated in a separate DR site.

The upgrade process includes the following steps: Backup your OneSign 3.x environment

·	Archive audit data. This will speed up the upgrade as less data will need to be migrated.

·	Upload all pre-requisite IPM’s and install a subset of them on the Failover and Primary  appliances (FA and PA), as preparation for the upgrade of OneSign itself. The order of steps is critical and is detailed in the Upgrading to OneSign 4.0 manual.

·	Upgrade OneSign on the PA to 4.0. This will shutdown OneSign so users will need to rely on offline mode. A new OneSign 4.0 enterprise is created with the former PA as the first appliance. This appliance is automatically designated as an Audit Server.

·	When this is done, you can bring the former PA up and resume operations. However, keep in mind that you only have one appliance, which is a single point of failure. You should backup your OneSign 4.0 environment immediately as you will not be able to restore an old 3.x backup into a OneSign 4.0 enterprise.

·	Once backup is complete and you are satisfied that everything is working, upgrade OneSign on the former FA to 4.0. It is automatically added to the enterprise and designated as a second Audit Server.

·	If you want to relocate one of the appliances and define a second site for it, you will need to delete it from the enterprise, physically relocate it, restage it, and then add it back to the enterprise (creating a new site for it in the process). During this procedure, you will only have one appliance serving users.

Upgrade from a 3.x primary-failover pair plus warm stand-by

Customers who have three OneSign 3.x appliances (two production and one stand-by) need to

decide whether they want to make all three appliances active after the upgrade or keep the former stand-by appliance as a backup for disaster recovery purposes.  If you define all three appliances in one site, then they will all be active and serve users. This can be done even if one appliance (the former stand-by) is physically in a separate location, as long as they are all on the same local network (because some users will work against this “remote” appliance). This provides more seamless redundancy because users failing over to another appliance within the same site do not have to re-authenticate.

If the former stand-by appliance is not on the local network, it is best to define it as a separate site, designated for disaster recovery. In this case, when adding this appliance to the enterprise, create a new site and then in the OneSign administrator UI designate it as a hot standby site. This will prevent OneSign agents from working against this appliance until they failover to it. Note that in this configuration, the former warm stand-by appliance is now serving as a hot standby – it is continuously synchronizing with the other appliances and agents will automatically fail over to it. Users will need to re-authenticate against it but no other action is needed, therefore providing higher availability than previously available.

In any case, the upgrade to V4.0 provides better end-user performance as both production appliances (and potentially also the third former stand-by appliance) are active and serving users.

The upgrade process includes the following steps:

·	Follow the above steps to upgrade the PA and FA.

·	Upgrade the former warm standby appliance to 4.0. It is being upgraded as a single appliance into a newly created enterprise, and thus will be designated as an audit server. You should then restage it and add it to the production enterprise of the former PA and FA (the information it contained is no longer needed as it will synchronize with the enterprise). As described above, you will need to either add it to the production site or create a new site for it.

·	Following the upgrade, you will have all three appliances designated as audit servers. You can reduce the amount of network traffic generated by having only two audit servers – one in the main site and one in the disaster recovery site. In order to do that, you will need to delete one of the main site appliances from the enterprise, restage it, and then add it back to the enterprise.

Post-upgrade considerations

Post upgrade, the LAN 2 port will no longer be used and you can unplug the crossover cable once both the PA and FA are upgraded.   During the upgrade, a new “superadmin” account is created to log into the Appliance Administrator (not the OneSign administrator). This “superadmin” account is the one that can add appliances to the OneSign Enterprise or remove them from it. The regular appliance “admin” account is kept but in 4.0 will have limited privileges – it can only manage one particular appliance. This allows you to give some lower level administrators the ability to do some appliance maintenance without them having the privilege to make changes to the entire OneSign Enterprise. After the upgrade, both the “admin” and “superadmin” accounts will have the same password as the “admin” account had originally. It is recommended that you change the “superadmin” password.

Virtual IP (VIP) changes

OneSign 4.0 failover intelligence is built into the agents (described further below in this document) and the V3.x VIP failover mechanism is no longer used. When upgrading, the VIP address is automatically assigned to the former Primary Appliance. It is recommended that you keep the virtual DNS name and IP address, as old 3.x agents and URL-based services such as the OneSign Self-Service portal will still point to the old settings. Because 3.x agents will only

point to one 4.0 appliance (the former PA), they will not have any failover capability until they are upgraded to 4.0. Similarly, services such as the OneSign Self-Service Portal, the OneSign Administrator UI, and other URL-based services will still work, but will not have built-in redundancy anymore. They should be handled as other web-based applications, for example using DNS zones. RADIUS clients (e.g. VPN servers) will need to be configured to use a second OneSign appliance as a failover RADIUS server.

Backup/restore limitations

You cannot restore 3.x backups on 4.0 or higher versions of OneSign. Therefore, it is strongly

recommended that you perform a 3.x backup before the upgrade and then a 4.0 backup on the former PA immediately after the upgrade, to create a baseline. Should you need to restore a 3.x backup, please contact Imprivata support. You will need to restore it to a 3.x appliance and then upgrade that appliance to 4.0 and create a 4.0 backup.

Kerberos changes

OneSign 4.0 uses a differently named Kerberos keytab file, which is shared among all the appliances. During an upgrade from 3.x to 4.0, the existing keytab file is deleted. You will need to re-generate and re-import a new keytab file after the upgrade is complete.

Agent installer changes

In v4.0, there are no longer different msi’s for each type of agent. The agent .msi installer is Type 1 by default. You may need to modify your push scripts to accommodate that.

IPTXPrimServer changes

IPTXPrimServer in 4.0 is used only for the initial bootstrapping, to download the enterprise

topology, and it is largely ignored after the topology is downloaded. If you need to point your agent to another OneSign enterprise, you can do either of the following:

·	Use the ForcePrimServer registry key to force the agent to communicate with a particular

appliance.

Note that, while the agent will download the new enterprise’s topology, this will force the agent to use only that one IPTXPrimServer server until the ForcePrimServer registry key is deleted.

·	Delete the agent’s offline data to force a bootstrap sequence. This is in “Documents and Settings\All Users\Application Data\SSOProvider\Offline”.

Top 10 items to note

Here are some things to be aware of before you implement OneSign 4.0:

A new license file is needed for V4.0 – contact Imprivata support to receive one. The license file will include all appliances in your enterprise, so you only need to download it once, when you create your enterprise.

Every OneSign enterprise should have at least 2 audit servers designated. An appliance can be designated as an audit server when it is added to the enterprise. The authorizing appliance in this case must be an Audit Server as well (unless there is none in the enterprise yet).

A new site can only be created when an appliance is added to the enterprise. Appliances cannot be moved within sites once they have been added to the enterprise.

Sites are related to computers and their IP addresses. When limiting the scope of an administrator to a site, there is no implications on which users that administrator can manage. To do the latter, limit the scope by domains or OU’s.

OneSign appliances communicate with each other by their real IP addresses only and set up firewall rules accordingly – there is no NAT support.

OneSign selects one of the appliances in the enterprise to perform scheduled synchronization with user directories. Therefore you should verify that each appliance has connectivity to at least one domain controller for each user directory, preferably on the same LAN.

OneSign 4.0 failover intelligence is built into the agents and the V3.x VIP failover mechanism is no longer used. When upgrading, you should assign the VIP address to one of the appliances. Old 3.x agents will only point to this appliance and so will not have any failover capability until they are upgraded to 4.0.

You cannot restore 3.x backups on 4.0 or higher versions of OneSign. Therefore, it is strongly recommended that you perform a 3.x backup before the upgrade and then a 4.0 backup on the former PA immediately after the upgrade, to create a baseline.

OneSign 4.0 uses a differently named Kerberos keytab file, which is shared among all the appliances. During an upgrade from 3.x to 4.0, the existing keytab file is deleted. You will need to re-generate and re-import a new keytab file after the upgrade is complete.

OneSign agents that failed over to another site do not automatically switch active sessions back to their home site after it has become available again. To force agents to failback active session, users need to lock and unlock their OneSign session, or log out and log back in.

Licensing

You will be asked to provide the initial license for the enterprise during the wizard process of the first appliance in the enterprise. This will include a license for all purchased appliances and only needs to be loaded once (not per appliance). The license is shared within the enterprise.

Thereafter, additional or updated licenses for future purchases need to be loaded from the OneSign administrator UI before you start the wizard process on new appliances. When such a new license is uploaded, OneSign verifies that at least one serial number in the new license matches the serial number of at least one appliance that is currently in the enterprise.  If not, then the license upload will be rejected.

Availability and appliance failover

Designating primary and secondary failover sites

For each site in your OneSign enterprise, you can designate a primary and a secondary failover sites. Go to the Sites tab under Properties and drill down to a specific site to set its failover sites. You do not specify failover rules at an appliance level. OneSign agents automatically fail over to appliances within the same site first and only then will fail over to a random appliance within the

failover sites specified. Users are always challenged when failing over to an appliance in another site (because a new OneSign session is established).

Agent determination of a Home Site

Each agent determines its home site based on the workstation’s IP configuration. According to

the OneSign enterprise topology, each site has a list of IP address ranges for subnets belonging to this site. The initial attempt to determine the agent’s home site involves matching the workstation IP address against any range in any site. If a range is found then the site owning this range is considered to be the home site for the agent. In case this direct IP matching fails, the agent analyzes the routing table on the workstation. The route lookup involves trying to find a route that covers any IP range for any site. Route lookup helps to determine location for a VPN client outside the corporate network when direct IP address matching does not work. IP ranges are not meant for restricting access – rather they help determine the preferred site to use. With this in mind, in most corporate environments there exists a non-default route to the corporate network and therefore for several sites with restrictive IP ranges within the corporate network sub-net, the first one will be chosen through the route rules.

Agent selection of appliance

OneSign 4.0 agents have a built-in intelligent mechanism for selecting an appliance. This section describes the rules by which an agent selects an appliance.When a deployed agent starts up for the first time, it retrieves the OneSign enterprise topology – the full configuration of appliance and sites. The IPTXPrimServer registry setting is used as the bootstrapping appliance for this purpose. After the topology is download, rules in the topology are used to find the server to be used in communication. If the enterprise topology changes the new topology is pushed to all the agents in the next update from the appliance.

The new topology will then be evaluated when a new session is started or on failover conditions.

The agent first attempts to connect to a random appliance in its home site. Once successful, it will keep using this appliance for new user sessions for a period of 24 hours. After 24 ours, the agent will attempt to connect to a different random server within its home site, for load balancing. If no other server is available, it will use the same server. However, this only applies to new sessions (e.g., upon user login) and does not affect active running sessions – they will remain served by the same appliance for performance reasons. Neither are active sessions impacted by any changes in the enterprise topology (as long as their appliance is still available).

If an agent cannot communicate with any appliance in its home site, it will try to failover to another site - first the primary, then the secondary failover sites, if specified by the administrator.

The agent will randomly choose appliances in the failover site and try to connect. If an agent cannot find any appliance to connect to, it will attempt to connect to the IPTXPrimServer appliance, which is the “last resort” appliance. This allows recovery from situations when the topology was completely misconfigured and the agent cannot connect to any server.

If an agent cannot communicate with an appliance through any of the means described above, it goes into off-line mode. The timeout for trying to connect to a server is set at 15 seconds. When an agent is on-line and attempting user authentication, the user will need to wait this long, per server tried according to above rules, until the agent decides to go off-line. Once the agent is off-line, further attempts to ping servers are done in the background (according to the interval set by the administrator), so there is no impact on the user.

Agents come back online once they succeed to connect through the process described above – on each ping or authentication attempt the agent will try all of these strategies. This accommodates for changes in routing table configurations.

Agent failback

Once all servers in the home site become unavailable, agents will switch to using a failover site

(if specified). After a failover was completed, the OneSign session will preserve the connection to the appliance in the failover site for the duration of the session lifetime.  Once appliances in the home site become available again, new sessions authenticated on computers that belong to this site will start connecting back to the home site. However, active sessions do not automatically switch back. To force agents to failback active session, users need to lock and unlock their OneSign session, or log out and log back in.

Agent connection examples

Example 1

Site 1 Site 2 Server 1-1 – 207.46.100.1 Server 2-1 – 207.46.200.1 Server 1-2 – 207.46.100.2 IP range – 207.46.100.1 – 207.46.100.255 IP range – 207.46.200.1 – 207.46.200.255 Failover: disabled Failover Site : Site 1

IPTXPrimServer: 207.46.100.2

Workstation 1: 207.46.100.105 Workstation 2: 207.46.200.12

In this example, assuming all servers are online, Workstation 1 will establish a connection with Site 1 (randomly selecting one of the servers) while Workstation 2 will connect to Site 2 according to IP addresses assigned to the workstation (Figure 2).

In case the Server 1-1 that was selected by Workstation 1 becomes unavailable, the agent will switch to the other server in Site 1 – Server 1-2 (Figure 3).

If Server 1-2 goes down as well, the agent goes offline as there are no failover sites defined for Site 1 and the IPTXPrimServer server and Server 1-2 are in fact the same appliance, and the agent already tried to connect to it once (Figure 4).

Now assume that all servers are currently up again and Workstation 2 is connected to Server 2

if this server goes offline a failover occurs to one of the servers in Site 1 because Site 1 is designated as the failover site for Site 2 (Figure 5).

Workstation 2

207.46.200.12

Figure 5

Once Server 2-1 in Site 2 becomes available again the existing session on Workstation 2 does not immediately fail back. However, once the user locks and unlocks or logs out and logs back in – a new connection is established within Site 2 as it is considered to be the home site.

Example 2

Site 1 Site 2 Server 1-1 – 207.46.100.1 Server 2-1 – 207.46.200.1 Server 1-2 – 207.46.100.2 IP range – 207.46.100.1 – 207.46.100.255 IP range – 207.46.200.1 – 207.46.200.255 Failover: disabled Failover Site: Site 1

Workstation IP Address: 10.10.1.1 Route table contains a non-default route to 207.46.100.255.

IPTXPrimServer: 207.46.100.2

In this example, although the workstation’s IP address does not fall into the ranges of any of the sites, there is a route that covers the IP range for Site 1 and this site is considered to be the home site (Figure 6).