Initial setup of a Nokia firewall

- Plug into serial port of firewall using supplied cable

- When powered on it will ask some preliminary questions such as admin password and if you want to set up an interface.

- Choose an interface that will be used for the web based Voyager management station to use to configure OS parameters.

- When prompted, give this interface, set duplex, speed, etc.

- Using a hub/switch or x-over cable, connect management PC to the Nokia device.

- Enter the ip address of the Nokia in the browser and enter “admin” and password when prompted.

- From here, set up all other interfaces under the “config” section of Voyager (web based config application).

- From here you can set up VRRP.  Usually you will use “monitored circuit” VRRP to allow you to monitor other interfaces.  Help pages are available on all screens via the “help” or “H” buttons.

- Upgrading software:

- Get the files onto the Nokia device using FTP.

- For IPSO (the OS) upgrade, use the “newimage –l imagename.tgz” command

- Remember to upgrade the documentation package with the OS.

- For Firewall-1 or any other package, use the “newpkg” command.  Follow the prompts.

- Packages are activated/deactivated under the “config/manage installed packages” in Voyager.

Setup of Checkpoint:

- Once you have installed and activated a checkpoint package, reboot firewall.

- Type “cd $FWDIR” to go into the firewall directory.

- Type “cpconfig”, this will ask you to specify the firewall software, keys, management IP addresses, admin passwords, etc.  Complete all tasks.