Physical to Virtual (P2V) Migration Process

Pre Migration Steps:

- Delete any un-necessary files.

  - Temp

  - Logs

  - Installations (remove / de-install, un-needed applications)

  - Performa a “Disk Cleanup” and Flush:

Temporary Internet Files

Office Setup Files

Recycle Bin

Temporary Files

WebClient / Publisher Temporary Files

Note:

Do NOT compress old files

- Export TCP/IP information(IPs, SNM, DFGW, SNM):

  - Open an RDP session to server

  - Open command prompt

  - Perform:

netsh -c interface dump > c:\servername.txt

route print > c:\servername.txt

Note:

Replace “servername” with the name of your server.

Migration Steps:

- Open VMware Converter

- Click Convert Machine

- Click Next

- Click Next

- Select “Physical Computer” from the drop down box then click next.

- Ensure the radio button “A Remote machine” is selected.

  - Enter the Name or IP address of the server you are converting.

  - Enter the User name / Password of who has administrative rights on the server.

  - Then Click Next

- The Converter agent will now be installed on the server.  If you are converting a Windows 2012 server, the agent will prompt for reboot of the server before you proceed with the conversion.  If you are converting a Windows 2012 server there is no reboot needed.

  - Click Yes to continue

  - The Agent will show its installing:

- Now you have the opportunity to resize the disk when it is converted to VM.

  - You can shrink or growth the volume at this time.

  - You can also select for multiple disk VM’s that it create separate disks for each volume. I would select this when given the option.

  - Leave “Ignore page file and hibernation file” checked

Then Click Next

- Click Next

- Now you need to select type: VMware Infrastructure Virtual Machine and then click next.

- Enter the ESX Host destination information

  - Server:

  - Username: root

  - Password: The password of the ESX Host

Then Click Next

- Enter the name of the Virtual Machine, and then click next.

- It should now confirm the ESX host which the VM is going to be created on, if good click next.

- Select the destination datastore where you to place the VM.

  - You can put the VM on one datastore or you can click the advanced button then select the datastore or datastores you want to use if you have multiple disks.

Click next when you have selected the disks.

- Select the VLAN or VSwitch the VM will be using.

  - Deselect Connect at Power on.

Click Next

- Check Install VMware Tools and Check Remove all system restore checkpoints and then click next.

- Click Finish to begin the process of the P2V, leave “Power on the new virtual machine after creation” unchecked.

- You will now see the P2V status.

- When the P2V is completed you will have a finished/completed status.

- Open the Virtual Center where the ESX host resides

- Locate the VM which you just created

- Click Edit Settings

- Remove any serial or parallel ports

- Remove Floppy Disk Drives

- Change CD/DVD Drive 1 to Client Device

- Delete CD/DVD’s if there is more than one

- Confirm RAM amount

- Confirm CPU’s

- Click on Network Adapter 1, Ensure Connect at power on is not checked and define Network Label. Network Label is the Port group which the VM will use.

- Click on any other Network Adapters, Ensure Connect at power on is not checked and define Network Label. Network Label is the Port group which the VM will use.

- Click OK

- Power on VM

- Open the VM console on VIC

- Login to server as local administrator/root

- Wait a minute or two and you will see the VMWare tools install it should prompt you for a restart, accept the reboot.

- Login to server as local administrator/root

- Delete any hidden NICs

  - Open Command Prompt

  - Type: set DEVMGR_SHOW_NONPRESENT_DEVICES=1

  - Press Enter

  - Type: DEVMGMT.MSC

  - Press Enter

  - When the Device Manager launches, choose View and select “Show Hidden Devices”

  - Delete the old NICS, you should see them as in a grayed out color.  Meaning they are not normal color.

  - Close out of DEVMGMT.MSC

- Uninstall any hardware based software.  Such as Dell Open Manage, Broadcom/Intel Management Tools.

- Now you need to configure the network interfaces on the VM.

  - You can manually enter values as obtained from the “Pre-Migration Steps” or

  - Copy file which you obtained from the “Pre-Migration Steps” to the VM “C” drive.

    - Open the file with notepad.

    - You will see text like:

# Interface IP Configuration for "Team 1"

set address name="Team 1" source=static addr=10.8.0.213 mask=255.255.254.0

add address name="Team 1" addr=10.8.0.214 mask=255.255.254.0

add address name="Team 1" addr=10.8.0.215 mask=255.255.254.0

add address name="Team 1" addr=10.8.0.216 mask=255.255.254.0

    - You will need to replace the “Team 1” with the name of the network interface inside of the VM. i.e.  “Public”

# Interface IP Configuration for "Public"

set address name="Public" source=static addr=10.8.0.213 mask=255.255.254.0

add address name="Public" addr=10.8.0.214 mask=255.255.254.0

add address name="Public" addr=10.8.0.215 mask=255.255.254.0

add address name="Public" addr=10.8.0.216 mask=255.255.254.0

    - Save the txt file

    - Open command Prompt

    - Netsh –f c:\servername.txt

    - Perform ipconfig to ensure the IP addresses have been added.

- Shutdown Physical Server

- Open command prompt from your PC and ping the physical server.  When the server stops responding continue.

- Edit Settings on VM

- Click on Network Interfaces and check the following:

  - Connect at power on

  - Connected

- Click OK

- From the command prompt on your PC you should now start seeing the ping response responding.

- Reboot VM

At this time you should be done with the P2V.  If you have to back out, you will need to shut down the VM and power on the physical server.