The Border Gateway Protocol (BGP) is the protocol backing the core routing decisions on the Internet. It maintains a table of IP networks or 'prefixes' which designate network reachability among autonomous systems (AS). It is described as a path vector protocol. BGP does not use traditional Interior Gateway Protocol (IGP) metrics, but makes routing decisions based on path, network policies and/or rulesets. For this reason, it is more appropriately termed a reachability protocol rather than routing protocol.

BGP was created to replace the Exterior Gateway Protocol (EGP) protocol to allow fully decentralized routing in order to transition from the core ARPAnet model to a decentralized system that included the NSFNET backbone and its associated regional networks. This allowed the Internet to become a truly decentralized system. Since 1994, version four of the BGP has been in use on the Internet. All previous versions are now obsolete. The major enhancement in version 4 was support of Classless Inter-Domain Routing and use of route aggregation to decrease the size of routing tables. Since January 2006, version 4 is codified in RFC 4271, which went through more than 20 drafts based on the earlier RFC 1771 version 4. RFC 4271 version corrected a number of errors, clarified ambiguities and brought the RFC much closer to industry practices.

Most Internet service providers must use BGP to establish routing between one another (especially if they are multihomed). Therefore, even though most Internet users do not use it directly, BGP is one of the most important protocols of the Internet. Compare this with Signaling System 7 (SS7), which is the inter-provider core call setup protocol on the PSTN. Very large private IP networks use BGP internally. An example would be the joining of a number of large OSPF (Open Shortest Path First) networks where OSPF by itself would not scale to size. Another reason to use BGP is multihoming a network for better redundancy either to multiple access points of a single ISP (RFC 1998) or to multiple ISPs.

Interior Gateway Routing Protocol (IGRP) is a distance vector interior routing protocol (IGP) invented by Cisco. It is used by routers to exchange routing data within an autonomous system.

IGRP is a proprietary protocol. IGRP was created in part to overcome the limitations of RIP (maximum hop count of only 15, and a single routing metric) when used within large networks. IGRP supports multiple metrics for each route, including bandwidth, delay, load, MTU, and reliability; to compare two routes these metrics are combined together into a single metric, using a formula which can be adjusted through the use of pre-set constants. The maximum hop count of IGRP-routed packets is 255 (default 100), and routing updates are broadcast every 90 seconds (by default).[1]

IGRP is considered a classful routing protocol. Because the protocol has no field for a subnet mask, the router assumes that all subnetwork addresses within the same Class A, Class B, or Class C network have the same subnet mask as the subnet mask configured for the interfaces in question. This contrasts with classless routing protocols that can use variable length subnet masks. Classful protocols have become less popular as they are wasteful of IP address space.

Enhanced Interior Gateway Routing Protocol - (EIGRP) is a Cisco proprietary routing protocol loosely based on their original IGRP. EIGRP is an advanced distance-vector routing protocol, with optimizations to minimize both the routing instability incurred after topology changes, as well as the use of bandwidth and processing power in the router. Routers that support EIGRP will automatically redistribute route information to IGRP neighbors by converting the 32 bit EIGRP metric to the 24 bit IGRP metric. Most of the routing optimizations are based on the Diffusing Update Algorithm (DUAL) work from SRI, which guarantees loop-free operation and provides a mechanism for fast convergence.

Open Shortest Path First (OSPF) is an adaptive routing protocol for Internet Protocol (IP) networks. It uses a link state routing algorithm and falls into the group of interior routing protocols, operating within a single autonomous system (AS). It is defined as OSPF Version 2 in RFC 2328 (1998) for IPv4.[1] The updates for IPv6 are specified as OSPF Version 3 in RFC 5340 (2008).[2]

OSPF is perhaps the most widely-used interior gateway protocol (IGP) in large enterprise networks. IS-IS, another link-state routing protocol, is more common in large service provider networks. The most widely-used exterior gateway protocol is the Border Gateway Protocol (BGP), the principal routing protocol between autonomous systems on the Internet.

# Routing Information Protocol

The Routing Information Protocol (RIP) is a distance-vector routing protocol, which employs the hop count as a routing metric. RIP prevents routing loops by implementing a limit on the number of hops allowed in a path from the source to a destination. The maximum number of hops allowed for RIP is 15. This hop limit, however, also limits the size of networks that RIP can support. A hop count of 16 is considered an infinite distance and used to deprecate inaccessible, inoperable, or otherwise undesirable routes in the selection process.

RIP implements the split horizon, route poisoning and holddown mechanisms to prevent incorrect routing information from being propagated. These are some of the stability features of RIP. It is also possible to use the so called RMTI[1] (Routing Information Protocol with Metric-based Topology Investigation) algorithm to cope with the count-to-infinity problem. With its help, it is possible to detect every possible loop with a very small computation effort.

Originally each RIP router transmitted full updates every 30 seconds. In the early deployments, routing tables were small enough that the traffic was not significant. As networks grew in size, however, it became evident there could be a massive traffic burst every 30 seconds, even if the routers had been initialized at random times. It was thought, as a result of random initialization, the routing updates would spread out in time, but this was not true in practice. Sally Floyd and Van Jacobson showed in 1994[2] that, without slight randomization of the update timer, the timers synchronized over time. In most current networking environments, RIP is not the preferred choice for routing as its time to converge and scalability are poor compared to EIGRP, OSPF, or IS-IS (the latter two being link-state routing protocols), and (without RMTI) a hop limit severely limits the size of network it can be used in. However, it is easy to configure, because RIP does not require any parameters on a router unlike other protocols (see here for an animation of basic RIP simulation visualizing RIP configuration and exchanging of Request and Response to discover new routes).

RIP is implemented on top of the User Datagram Protocol as its transport protocol. It is assigned the reserved port number 520.[3]