Title here

2k Secure baseline Configuration Standards

System Name

Implementation Review/Approval Sheet

____________________________________  ______/_____/_____

System Administrator

____________________________________  ______/_____/_____

Security Certifier

____________________________________  ______/_____/_____

System Owner

Prepared by:

For:

TABLE OF CONTENTS

1.0	Account Policies	8

1.1.	Password Strength	8

1.2.	Password Length	8

1.3.	Password Minimum Age	8

1.4.	Password Maximum Age	8

1.5.	Password Reversible Encryption	8

1.6.	Account Lockout Duration	9

1.7.	Account Lockout Threshold	9

1.8.	Reset Account Lockout	9

1.9.	Rename Administrator Account	9

1.10.	Disable Guest Account	9

2.0	Local Policies	10

2.1.	Audit Account Logon Events	10

2.2.	Audit Account Management	10

2.3.	Audit Directory Services Access	10

2.4.	Audit Logon Events	10

2.5.	Audit Object Access	10

2.6.	Audit Policy Change	10

2.7.	Audit Privilege Use	11

2.8.	Audit System Events	11

2.9.	Maximum Application Log Size	11

2.10.	Maximum Security Log Size	11

2.11.	Maximum System Log Size	11

2.12.	Restrict Guest Access to All Logs	11

2.13.	Retention Method For Logs	12

2.14.	Shutdown Computer When Security Log Full	12

2.15.	Restrictions For Anonymous Connections	12

2.16.	Allow Server Operators to Schedule Tasks	12

2.17.	Allow System Shut Down Without Logon	13

2.18.	Allowed to Eject Removable NTFS Media	13

2.19.	Amount of Idle Time Before Session Disconnect	13

2.20.	Audit Access of Global System Objects	13

2.21.	Audit Use of Backup and Restore	13

2.22.	Automatically Log Off Users	14

2.23.	Clear Virtual Memory on Shut Down	14

2.24.	Digitally Sign Client Communications	14

2.25.	Digitally Sign Server Communications	14

2.26.	Disable CTL+ALT+DEL For Logon	14

2.27.	Do Not Display Last User Name In Logon Screen	15

2.28.	LAN Manager Authentication Level	15

2.29.	Message Text For Users Attempting Logon	15

2.30.	Message Title For Users Attempting Logon	15

2.31.	Number of Previous Logons To Cache	15

2.32.	Prevent System Maintenance Of Account Password	15

2.33.	Prevent Users From Installing Print Drivers	15

2.34.	Prompt User To Change Password	16

2.35.	Recovery Console (Allow Administrative Logon)	16

2.36.	Recovery Console (Allow Access To All Drives)	16

2.37.	Rename Administrator Account	16

2.38.	Rename Guest Account	16

2.39.	Restrict Removable Media Access	16

2.40.	Digitally Encrypt Secure Channels	17

2.41.	Require Strong 2K Session Keys	17

2.42.	Send Unencrypted Passwords To Third Party SMB Server	17

2.43.	Shut Down System Immediately If Unable To Log Security	17

2.44.	Smart Card Behavior	17

2.45.	Strengthen Default Global Permissions	17

3.0	Services	18

3.1.	Computer Browser	18

3.2.	NTLM Security Support Provider	18

3.3.	SNMP Service	18

3.4.	Terminal Services	18

3.5.	Windows Management Instrumentation	19

3.6.	Messenger and Alerter Services	19

3.7.	Telnet Service	19

3.8.	FTP Service	19

3.9.	Trivial FTPD	19

3.10.	Simple TCP/IP	20

3.11.	TCP/IP Print Server	20

3.12.	QOS RSVP	20

3.13.	Clip Book	20

3.14.	Fax Service	20

3.15.	Indexing	20

3.16.	Enabled Services List	21

3.17.	Net Meeting Remote Desktop Sharing	21

4.0	Registry Settings	22

4.1.	Resilience to Distributed Denial of Service Attacks	22

4.2.	Handling Half-Open HTTP and FTP Requests	22

4.3.	Protection Against Discovery of NetBIOS Name	23

4.4.	Disable The Use of 8.3 File Name Conventions	23

4.5.	Disable Autorun On CDROM Drives	23

4.6.	Remove The OS2 And POSIX Subsystems	23

4.7.	Eliminate Screen Saver Grace Period	24

4.8.	Protection of Kernel Object Attributes	24

4.9.	Restrict Null Access to Shares	24

4.10.	Event Log 90% Full Warning	24

4.11.	Bypass Cached Credentials Without Upgrading Privileges	24

4.12.	Disable LM Hash Creation	25

5.0	Configure IPSEC	26

5.1.	Add Packet Filters Using IPSEC	26

5.2.	Add Block All with IPSEC	26

5.3.	Assign IPSEC Policy	26

5.4.	Add Block All with IPSEC	27

6.0	Files and Permissions	28

6.1.	Move CMD.EXE	28

6.2.	Move FINGER.EXE	28

6.3.	Move NBTSTAT.EXE	28

6.4.	Move NETSTAT.EXE	28

6.5.	Move RSH.EXE	28

6.6.	Move RCP.EXE	28

6.7.	Move ROUTE.EXE	29

6.8.	Move TELNET.EXE	29

6.9.	Move TFTP.EXE	29

6.10.	Move TRACERT.EXE	29

6.11.	Move COMMAND.COM	29

6.12.	Remove DOS Files	29

6.13.	Remove OS/2 Subsystem Files	30

6.14.	Remove POSIX Subsystem	30

6.15.	Move NET.EXE	30

6.16.	Move IPCONFIG.EXE	30

6.17.	Move PING.EXE	30

6.18.	Move REGEDT32.EXE	30

6.19.	Change File Permissions All Risk Categories	31

7.0	USER RIGHTS POLICY CONFIGURATION	33

8.0	GENERAL SECURITY	35

8.1.	Install Antivirus	35

8.2.	Create NTFS Volumes And Disks	35

8.3.	Windows Update	35

8.4.	Do Not Allow Automatic Logons	35

8.5.	Install Dummy Administrator Account	35

8.6.	Remove Power Users	36

8.7.	Remove Local Accounts From Domain Member Wks	36

8.8.	 Remove Default Shares From Workstations	36

8.9.	Remove Modems From Workstations	36

8.10.	Replace Everyone Group With Auth Users	36

8.11.	Create Security Group – Set Permissions On Logs	36

8.12.	Enable Startup Password	37

8.13.	Install Service Applications Off The Root Drive	37

FORWARD

This document is designed to provide 2K system administrators with a quick and concise set of procedures to follow when first setting up and securing a new server.  The security controls described here are intended to be used on file servers, web servers, database servers and other systems that are not intended for interactive logon by average users.  All recommendations in this document should be thoroughly tested on non-production servers to verify that they will not impact the functionality of critical systems and networks.

These changes should be made in the following order:

- Download all applicable Service Packs and Hotfixes from Microsoft.com and burn them to a CD-ROM.

- Disconnect computer system from any network(s).

- Install 2K onto system, reformatting the hard drives with NTFS.

- Make changes to system BIOS, if desired.

- Install all Service Packs and Hotfixes from CD-ROM.

- Install any additional drivers for computer hardware.

- Enable auditing.

- Implement account policies and system security policies.

- Configure registry permissions and auditing.

- Configure file permissions.

- Configure additional application security controls.

- Install and configure additional event log security.

- Install Anti-Virus software and up-to-date virus signatures.

- Reconnect to network.

At no time should the computer be connected to any network until all security changes have been made.  After configuring 2K according to these guidelines, image the file system using an application such as Ghost so that the image can be deployed for all new systems. This guideline for securing 2K systems documents the security features applied to  [SYSTEM NAME].  The guidelines are meant for implementation on a 2K system in one of three levels determined by a preliminary system risk evaluation. The risk levels are high, medium, and low.

Risk Determination (Quick Look)

The risk determination is depicted in the illustration above as being a function of threat, vulnerability, and exposure. It can be used to quickly look at a proposed 2K deployment and sufficiently judge its inherent risk level based on the critically of the system (confidentiality, integrity, and availability requirements), the threat to the system (internal, external, natural, and malicious), the vulnerability of the system (including current and potential future vulnerability), and the exposure to the threat (internet facing, other security controls).

Because threats to computer systems are almost always prevalent, another way to depict the above chart is by using two components of the risk = vulnerabilities × exposures × threat formula. These two components are exposure and vulnerability. As exposure and vulnerabilities increase, so does risk.

High Risk.  It is likely that exploitation of a given vulnerability by a threat will severely and adversely affect a system, tangible and intangible resources or do harm to the reputation of the Department of Transportation.  This level of risk requires strong implementation measures, and actions and guidance under risk category H should be followed.

Moderate Risk.  It is likely that exploitation of the identified vulnerability by a threat will moderately affect the system indicating the loss of some tangible assets or resources, or become damaging to the reputation of the Department of Transportation. This level of risk requires moderately strong implementation measures, and actions and guidance under risk category M should be followed.

Low Risk.  The identified weaknesses may be subject to exploitation by a threat, but the probability of exploitation is low, and the impact would be minor.  This level of risk indicates that management should be cautioned and corrective measures be applied where required. This level of risk requires core implementation measures, and actions and guidance under risk category L should be followed.

Figure 1: Risk Matrix Examples

| Purpose | Quick Look Risk Rating |
| --- | --- |
| Mail Server, Web Server, DNS Server (Sensitive and Internet Facing) | HIGH |
| Domain Server, HR Database, Financials, Targets of Opportunity/Choice (CSIRC, Network Monitoring Servers, Helpdesk), Patient Database, Classified server. | HIGH |
| Firewall, Content Server, Proxy Server | HIGH |
| DHCP Server, Internal Mail Server (behind other security controls), Mobile Laptops | MODERATE |
| Development Server (Internal behind FW and other security controls), RRAS (behind other security controls) File Servers | MODERATE |
| User Desktop (behind other security controls) | MODERATE |
| Isolated Systems where network access controls allow for no incoming service request | LOW |
| Systems protected by a comprehensive security suite that includes workstation firewalls, intrusion detection, and constant monitoring with quick response time to incidents. | LOW |

# Account Policies

| Password Strength |
| --- |
| Description | Action | Required |
| Securing your environment requires strong passwords. Mix upper and lower case with special characters. Do not use names, words found in the dictionary, or license plate numbers. | Under Control Panel, Administrative Tools, Security Policies, Account Policies, Password Policy – Enable “Passwords must meet complexity requirements.” | L | M | H |
| Password Length |
| Description | Action | Required |
| Securing your environment requires strong passwords. | Under Control Panel, Administrative Tools, Security Policies, Account Policies, Password Length – Set to at least 8 characters (or greater if require by local policy). | L | M | H |
| Password Minimum Age |
| Description | Action | Required |
| The minimum password age specifies the minimum amount of time a user must keep his or her password in effect. This prevents users from using a script to rotate through the password history and reuse an old password. | Under Control Panel, Administrative Tools, Security Policies, Account Policies, Password Policy – Set to 2 Days | L | M | H |
| Password Maximum Age |
| Description | Action | Required |
| The maximum password age establishes the amount of time before the system requires a user to change their password. | Under Control Panel, Administrative Tools, Security Policies, Account Policies, Password Policy – Set Maximum password age to 90 Days Set Maximum password age to 60 Days Set Maximum password age to 30 days Note: Under DOT Policy, administrators must change their passwords at least every 30 days. Since 2K lacks the ability to specify different parameters for different accounts, this must be enforced procedurally. | L | M | H |
| Password Reversible Encryption |
| Warning. This policy should never be enabled unless application requirements are greater than the need to protect password information. In MOST cases, the policy should be DISABLED, as shown below. |
| Description | Action | Required |
| Reversible encryption stores the password in a weaker form than normal. Some applications may require access to user passwords to provide additional functionality and use reversible encryption. | Under Control Panel, Administrative Tools, Security Policies, Account Policies, Password Policy – Set “Store password using reversible encryption” to DISABLED | L | M | H |
| Account Lockout Duration |
| Description | Action | Required |
| The account lockout duration determines the number of minutes the account remains unavailable. | Under Control Panel, Administrative Tools, Security Policies, Account Policies, Account Lockout Policy – Set Account Lockout Duration to 30 minutes Set Account Lockout Duration to 1 Hour Set Account Lockout Duration to 2 Hours | L | M | H |
| Account Lockout Threshold |
| WARNING! A malicious attacker could intentionally or inadvertently cause a denial of service condition by attacking all user accounts with a brute force password tool. However, where the protection of confidentiality and integrity are important, this is considered a prudent and necessary control measure. |
| Description | Action | Required |
| Password attacks are often automated “guessing” programs that can brute force user passwords. The threshold setting can help deter password compromise. | Under Control Panel, Administrative Tools, Security Policies, Account Policies, Account Lockout Policy – Set Account Lockout Threshold to 5. | L | M | H |
| Reset Account Lockout |
| Description | Action | Required |
| Users may sometimes accidentally forget their passwords and lock themselves out of the system. This setting allows them to wait a minimum amount of time and try again. Must be set lower than or equal to the Account lockout duration. | Under Control Panel, Administrative Tools, Security Policies, Account Policies, Password Policy – Set Reset Account lockout to 20 minutes. Set Equal to Account Lockout | L | M | H |
| Rename Administrator Account |
| Description | Action | Required |
| Rename the Administrator account to prevent an attacker from easily guessing the Administrator username. Create a dummy administrator account to log attempted accesses. | Under Control Panel, Administrative Tools, Computer Management, System Tools, Local Users and Groups, Users— Rename Administrator account and create a dummy Administrator account with no privileges. | L | M | H |
| Disable Guest Account |
| Description | Action | Required |
| The Guest account should be disabled to prevent access to unauthorized users. A malicious user could use this account and escalate privileges or insert malware onto the system. | The Guest account is disabled by default. Under Control Panel, Administrative Tools, Computer Management, System Tools, Local Users and Groups, Users— Ensure that the Guest account is disabled. Add a strong password to the disabled account. | L | M | H |

# Local Policies

| Audit Account Logon Events |
| --- |
| Description | Action | Required |
| This provides a method of tracking user logon and logout activities. | Under Control Panel, Administrative Tools, Local Security Policy, Local Policies, Audit Policy – Set Audit account logon events to Success, Failure | L | M | H |
| Audit Account Management |
| Description | Action | Required |
| This action provides a method of tracking management actions, like creating new users. | Under Control Panel, Administrative Tools, Local Security Policy, Local Policies, Audit Policy – Set Audit account management to Success, Failure | L | M | H |
| Audit Directory Services Access |
| Description | Action | Required |
| This feature provides a method of tracking access to the 2K Active Directory. | Under Control Panel, Administrative Tools, Local Security Policy, Local Policies, Audit Policy – Set Audit directory service access to Success, Failure. | L | M | H |
| Audit Logon Events |
| Description | Action | Required |
| This feature allows for the tracking of logon events and is useful in forensic analyses after a system has been compromised. | Under Control Panel, Administrative Tools, Local Security Policy, Local Policies, Audit Policy – Set Audit logon events to Success, Failure | L | M | H |
| Audit Object Access |
| Information! Setting this policy does not automatically audit access to objects, nor does it automatically use system resources. You must set a success or failure attribute directly on the file or registry key that you need to monitor, using Windows Explorer or a command line tool such as Xcacls.exe. |
| Description | Action | Required |
| This feature allows for the tracking of access to system objects like specifically defined files, folders, or hardware like printers. | Under Control Panel, Administrative Tools, Local Security Policy, Local Policies, Audit Policy – Set Audit object access to Success, Failure | L | M | H |
| Audit Policy Change |
| Description | Action | Required |
| This feature is used to monitor policy changes and can be used as an early warning indication that event logging has been disabled. | Under Control Panel, Administrative Tools, Local Security Policy, Local Policies, Audit Policy – Set Audit policy change to Success, Failure | L | M | H |
| Audit Privilege Use |
| WARNING! Setting this feature to success will audit all privileged use on the system and will fill event logs quickly when the system has multiple users. |
| Description | Action | Optional |
| This feature can be used to track user attempts to exercise privileges on file systems, folders, and objects. | Under Control Panel, Administrative Tools, Local Security Policy, Local Policies, Audit Policy – Set Audit privilege use to Failure Due to the potential impact to the system, this is an optional control, but its use is encouraged for moderate to high risk systems. | L | M | H |
| Audit System Events |
| Description | Action | Required |
| Used to track system events like services starting and stopping. Can be very useful in troubleshooting problems with servers and processes. | Under Control Panel, Administrative Tools, Local Security Policy, Local Policies, Audit Policy – Set Audit system events to Success, Failure. | L | M | H |
| Maximum Application Log Size |
| Description | Action | Required |
| Sets the Maximum size of this event log. | Under Control Panel, Administrative Tools, Local Security Policy, Local Policies, Audit Policy – Set maximum application log size to 10240 KB*. Depends on disk size and number of expected events. This is given as an example. This field may only be present if a security policy template has been loaded and implemented. | L | M | H |
| Maximum Security Log Size |
| Description | Action | Required |
| Sets the Maximum size of this event log. | Under Control Panel, Administrative Tools, Local Security Policy, Local Policies, Audit Policy – Set maximum security log size to 18.5 MB* Depends on disk size and number of expected events. This is given as an example. This field may only be present if a security policy template has been loaded and implemented. | L | M | H |
| Maximum System Log Size |
| Description | Action | Required |
| Sets the Maximum size of this event log. | Under Control Panel, Administrative Tools, Local Security Policy, Local Policies, Audit Policy – Set maximum system log size to 10240 KB*. Depends on disk size and number of expected events. This is given as an example. This field may only be present if a security policy template has been loaded and implemented. | L | M | H |
| Restrict Guest Access to All Logs |
| Description | Action | Required |
| This feature when set will disable guest access to system and security logs. | Under Control Panel, Administrative Tools, Local Security Policy, Local Policies, Audit Policy – Set restrict guest access to system log to ENABLED* Set restrict guest access to security log to ENABLED* Set restrict guest access to application log to ENABLED* This is given as an example. This field may only be present if a security policy template has been loaded and implemented. | L | M | H |
| Retention Method For Logs |
| Description | Action | Required |
| This feature allows the administrator to choose how log files will archived, rotated, or retained for backup. Options are: Overwrite events by days. Overwrite events as needed. Manually clear logs. Not defined. | Under Control Panel, Administrative Tools, Local Security Policy, Local Policies, Audit Policy – Set retention method for security log to Overwrite in 30 Days * Set retention method for application log to Manually Clear Logs * This is given as an example. This field may only be present if a security policy template has been loaded and implemented. | L | M | H |
| Shutdown Computer When Security Log Full |
| WARNING! Setting this feature to ENABLED will place an extreme burden on system administrators and help desk personnel in a large computing environment. In most cases, it should be set to Disabled, as shown below. |
| Description | Action | Required |
| This setting allows an administrator to have the system shut down if an audit security log becomes full of events. It is meant to combat a determined system attack. | Under Control Panel, Administrative Tools, Local Security Policy, Local Policies, Audit Policy – Set shut down the computer when the security audit log is full to DISABLED. | L | M | H |
| Restrictions For Anonymous Connections |
| Description | Action | Required |
| By default, 2K allows anonymous users to enumerate the names of domain accounts and network shares. This may allow an intruder to gain vital information to further attack the network. This feature is used to control that behavior. | Under Control Panel, Administrative Tools, Local Security Policy, Local Policies, Security Options – Set additional restrictions for anonymous connections to Do not allow enumeration of SAM accounts and shares. Edit registry setting HKLM\SYSTEM\CurrentControlSet\Control\LSA RestrictAnonymous (value 1) | L | M | H |
| Allow Server Operators to Schedule Tasks |
| Description | Action | Required |
| This feature allows operators (Users) the ability to run the MS scheduler. This can be dangerous as an attacker can run scheduled tasks to send out nefarious emails, passwords, or sensitive information. | Under Control Panel, Administrative Tools, Local Security Policy, Local Policies, Security Options – Set Allow server operators to schedule tasks to DISABLED. (applies to Domain Controller only) | L | M | H |
| Allow System Shut Down Without Logon |
| Description | Action | Required |
| This feature allows for shut down of the computer without logging on. | Under Control Panel, Administrative Tools, Local Security Policy, Local Policies, Security Options – Set Allow system to be shut down without having to log on to DISABLED. | L | M | H |
| Allowed to Eject Removable NTFS Media |
| Description | Action | Required |
| This feature allows for users to eject NTFS formatted devices/media. An attacker could remove media from one machine where there is only user privileges to another machine where there is administrator privileges and gain access to sensitive information. | Under Control Panel, Administrative Tools, Local Security Policy, Local Policies, Security Options – Set Allowed to eject removable NTFS media to Administrators. | L | M | H |
| Amount of Idle Time Before Session Disconnect |
| Description | Action | Required |
| Each server message block (SMB) session consumes server resources. An attacker could repeatedly establish SMB sessions causing a denial of service. | Under Control Panel, Administrative Tools, Local Security Policy, Local Policies, Security Options – Set amount of idle time before disconnect to 15 minutes. | L | M | H |
| Audit Access of Global System Objects |
| Description | Action | Required |
| This feature allows for the auditing of mutexes, events, semaphores, and DOS devices. | Under Control Panel, Administrative Tools, Local Security Policy, Local Policies, Security Options – Set audit access of global system objects to DISABLED. Set audit access of global system objects to ENABLED in classified environments. | L | M | H |
| Audit Use of Backup and Restore |
| WARNING! Setting this feature to ENABLED will record every file backed up or restored and can fill the system security log. |
| Information! You can use this feature along with hash values to determine the last known good backup of a particular file or folder before a compromise. However, the security log will be large. It is also good for troubleshooting backup and restore operations. |
| Description | Action | Required |
| Use of this feature when the Audit Privilege Use feature is turned on can enable the administrator to audit malicious behavior of someone restoring files inappropriately. | Under Control Panel, Administrative Tools, Local Security Policy, Local Policies, Security Options – Set Audit Use of Backup and Restore to DISABLED. | L | M | H |
| Automatically Log Off Users |
| Information! You can use this feature for users only. It does not apply to Administrators. |
| Description | Action | Required |
| This setting affects the SMB component of a 2K server. If a clients’ logon hours are expired, it forces a logoff. | Under Control Panel, Administrative Tools, Local Security Policy, Local Policies, Security Options – Set to ENABLED | L | M | H |
| Clear Virtual Memory on Shut Down |
| Description | Action | Required |
| To help Windows with multitasking functions, the pagefile may have sensitive information dumped to it, including passwords, emails, and documents. | Under Control Panel, Administrative Tools, Local Security Policy, Local Policies, Security Options – Set Clear Virtual Memory Page File When System Shuts Down to ENABLED. | L | M | H |
| Digitally Sign Client Communications |
| WARNING! Setting this feature to ENABLED will add a 15% overhead to each packet sent and received. This may have serious performance issues on large networks and should typically only be deployed on networks requiring high security. |
| Description | Action | Required |
| SMB signing authenticates both the server and user hosting the data. Implementing this feature in high security networks helps to prevent session hijacking. | Under Control Panel, Administrative Tools, Local Security Policy, Local Policies, Security Options – Set digitally sign client communications (always) to DISABLED. Set digitally sign client communications (when possible) to ENABLED. | L | M | H |
| Digitally Sign Server Communications |
| WARNING! Setting this feature to ENABLED will add a 15% overhead to each packet sent and received. This may have serious performance issues on large networks and should typically only be deployed on networks requiring high security. |
| Description | Action | Required |
| SMB signing authenticates both the server and user hosting the data. Implementing this feature in high security networks helps to prevent session hijacking. | Under Control Panel, Administrative Tools, Local Security Policy, Local Policies, Security Options – Set digitally sign server communications (always) to DISABLED. Set digitally sign server communications (when possible) to ENABLED. | L | M | H |
| Disable CTL+ALT+DEL For Logon |
| Description | Action | Required |
| Requiring the use of CTRL+ALT+DEL for logon ensures that users are communicating via a trusted path when entering their passwords. | Under Control Panel, Administrative Tools, Local Security Policy, Local Policies, Security Options – Set disable ctrl+alt+del to DISABLED. | L | M | H |
| Do Not Display Last User Name In Logon Screen |
| Description | Action | Required |
| A malicious person with physical access to a computer could gain username information and later run automated brute force tools to compromise an account. | Under Control Panel, Administrative Tools, Local Security Policy, Local Policies, Security Options – Set do not display last user name to ENABLED. | L | M | H |
| LAN Manager Authentication Level |
| WARNING! In some situations, Setting this feature to NTLMV2 may break 2K servers in a cluster configuration. This must be tested in advance of deployment. |
| Description | Action | Required |
| LM, NTLM, and NTLMv2 allows authentication on to the network and between the DC and client computers. NTLMv2 is the strongest authentication mechanism. | Under Control Panel, Administrative Tools, Local Security Policy, Local Policies, Security Options – Set LAN Manager authentication to NTLMV2. Note: NTLMV2 is not compatible with older versions of Windows. This can only be enabled for a network that runs exclusively 2K and above. | L | M | H |
| Message Text For Users Attempting Logon |
| Description | Action | Required |
| This feature provides criminal trespass warnings for those that unlawfully enter your system. | Under Control Panel, Administrative Tools, Local Security Policy, Local Policies, Security Options – Set to USER DEFINED TEXT to contain the standard DOT security banner. | L | M | H |
| Message Title For Users Attempting Logon |
| Description | Action | Required |
| This feature provides criminal trespass warnings for those that unlawfully enter your system. | Under Control Panel, Administrative Tools, Local Security Policy, Local Policies, Security Options – Set to USER DEFINED TEXT to read similar to: “WARNING: THIS IS A U.S. DEPARTMENT OF TRANSPORTATION COMPUTER SYSTEM:” | L | M | H |
| Number of Previous Logons To Cache |
| Description | Action | Required |
| This features places the number of users logons into an encrypted cache spread throughout the registry in different location. If set to 10, 10 users will have logon information cached. | Under Control Panel, Administrative Tools, Local Security Policy, Local Policies, Security Options – Set number of previous logons to cache to 0. | L | M | H |
| Prevent System Maintenance Of Account Password |
| Description | Action | Required |
| This feature controls windows computer password accounts on a domain. | Under Control Panel, Administrative Tools, Local Security Policy, Local Policies, Security Options – Set prevent system maintenance of account password to DISABLED. | L | M | H |
| Prevent Users From Installing Print Drivers |
| Description | Action | Required |
| This feature should only be allowed by administrators. | Under Control Panel, Administrative Tools, Local Security Policy, Local Policies, Security Options – Set prevent users from installing print drivers to ENABLED. | L | M | H |
| Prompt User To Change Password |
| Description | Action | Required |
| This is a reminder feature designed to let users know their accounts will be disabled if they do not change their password within XX days. | Under Control Panel, Administrative Tools, Local Security Policy, Local Policies, Security Options – Set prompt user to change password to 14 days. | L | M | H |
| Recovery Console (Allow Administrative Logon) |
| Description | Action | Required |
| The recovery console is used to troubleshoot systems that will not reboot or start. | Under Control Panel, Administrative Tools, Local Security Policy, Local Policies, Security Options – Set recovery console: allow automatic administrative access to DISABLED. | L | M | H |
| Recovery Console (Allow Access To All Drives) |
| Description | Action | Required |
| This feature is used to stop inadvertent booting of the OS when the OS disk has been left in the CDROM, or when an administrative disk containing sensitive information has been left in the CDROM drive. | Under Control Panel, Administrative Tools, Local Security Policy, Local Policies, Security Options – Set recovery console: allow floppy copy and access to all drives and folders to DISABLED. | L | M | H |
| Rename Administrator Account |
| Description | Action | Required |
| Rename the Administrator account to prevent an attacker from easily guessing the Administrator username. Create a dummy administrator account to log attempted accesses. | Under Control Panel, Administrative Tools, Local Security Policy, Local Policies, Security Options – Set new Administrator name. | L | M | H |
| Rename Guest Account |
| Description | Action | Required |
| The Guest account should be disabled to prevent access to unauthorized users. A malicious user could use this account and escalate privileges or insert malware onto the system. | The Guest account is disabled by default. Under Control Panel, Administrative Tools, Computer Management, System Tools, Local Users and Groups, Users— Ensure that the Guest account is disabled. | L | M | H |
| Restrict Removable Media Access |
| Description | Action | Required |
| These features apply to local access to floppy and CDROM drives. Setting to enabled will prevent remote users from accessing removable media. | Under Control Panel, Administrative Tools, Local Security Policy, Local Policies, Security Options – Set restrict access to locally logged on user for CDROM and FLOPPY to ENABLED. | L | M | H |
| Digitally Encrypt Secure Channels |
| Information! This feature is only supported by NT4.0 SP6a and later. Expected a small increase in network overhead. Down level domains may not be able to participate. This feature should be used between ALL machines, but only where high security is required, for extremely high requirements for protection of confidentiality and integrity. |
| Description | Action | Required |
| These features are used when negotiating with the domain for account logon. The account password is used to establish the secure channel. | Under Control Panel, Administrative Tools, Local Security Policy, Local Policies, Security Options – Set digitally encrypt or sign always to DISABLED. Set digitally sign or encrypt when possible to ENABLED. | L | M | H |
| Require Strong 2K Session Keys |
| Description | Action | Required |
| The 2K session keys are much stronger and should be used whenever possible. | Under Control Panel, Administrative Tools, Local Security Policy, Local Policies, Security Options – Set secure channel: require strong 2K session keys to ENABLED. | L | M | H |
| Send Unencrypted Passwords To Third Party SMB Server |
| Description | Action | Required |
| If this feature is enabled, plain text passwords can be sent to third party SMB servers. Plain text passwords are subject to capture and reuse. | Under Control Panel, Administrative Tools, Local Security Policy, Local Policies, Security Options – Set send unencrypted passwords to third party smb servers to DISABLED. | L | M | H |
| Shut Down System Immediately If Unable To Log Security |
| Description | Action | Required |
| This setting is disabled to prevent an attacker from causing a denial of service. Only enable on high security networks where logs are monitored 24x7. | Under Control Panel, Administrative Tools, Local Security Policy, Local Policies, Security Options – Set to DISABLED. Set to ENABLED. | L | M | H |
| Smart Card Behavior |
| Description | Action | Required |
| If smart cards are being used and this setting is enabled, the machine will lockup until the smart card is reinstalled. | Under Control Panel, Administrative Tools, Local Security Policy, Local Policies, Security Options – Set smart card removal behavior to ENABLED. | L | M | H |
| Strengthen Default Global Permissions |
| Description | Action | Required |
| This setting is to control and strengthen the discretionary access controls list placed on shares, semaphores, and devices. If enabled, non-administrators will have only read access to shared objects that they do not create. | Under Control Panel, Administrative Tools, Local Security Policy, Local Policies, Security Options – Set strengthen default permissions of global objects to ENABLED. | L | M | H |

# Services

Any service or application is a potential point of attack. Any unneeded services or executables should be disabled or removed from the system. It is important to remember that systems should be role secured  based upon their risk factor to the network. This means that a web servers security posture will be totally different than a desktop or mail server, and that its services will be different.

| Computer Browser |
| --- |
| Description | Action | Required |
| The computer browser is used to serve information about the domain, shares, and systems to whomever request the information. | Under Control Panel, Services – Set service mode to AUTOMATIC in low risk and moderate risk environments. Set to MANUAL in high risk environments or DISABLED. | L | M | H |
| NTLM Security Support Provider |
| Description | Action | Required |
| This service provides backward compatibility for applications that require it. NTLM RPC service support is now include in the CORE OS. | Under Control Panel, Services – Set this service to DISABLED if not required by older applications. | L | M | H |
| SNMP Service |
| Description | Action | Required |
| This service is not installed by default, but is often used by Network Engineers and Administrators. | Under Control Panel, Services – Set this service to DISABLED unless needed. | L | M | H |
| Terminal Services |
| Description | Action | Required |
| This service allows for the remote administration of the server. Only enable this service if access is controlled to port 3389 via source address. | Under Control Panel, Services – Set this service to DISABLED unless source address request can be controlled. | L | M | H |
| Windows Management Instrumentation |
| Description | Action | Required |
| This service is required for managing logical disks that use computer management. It also facilitates performance alerts. Turning this service off may keep some applications from working. | Under Control Panel, Services – Set this service to AUTOMATIC | L | M | H |
| Messenger and Alerter Services |
| Description | Action | Required |
| These services control net send and net name commands. | Under Control Panel, Services – Set these services to DISABLED. | L | M | H |
| Telnet Service |
| Description | Action | Required |
| This service is often installed by Administrators and Network Engineers. This service should be removed or disabled and SSH server should be installed. | Under Control Panel, Services – Remove or DISABLE the service. | L | M | H |
| FTP Service |
| Description | Action | Required |
| This service is often installed with IIS. It passes passwords in clear text. Disable the service and install a SSH server. | Under Control Panel, Services – Set this service to DISABLED. | L | M | H |
| Trivial FTPD |
| Description | Action | Required |
| This service is typically installed by Network administrators and should be disabled to prevent malicious code or sensitive information from being compromised. | Under Control Panel, Services – Remove this service. | L | M | H |
| Simple TCP/IP |
| Description | Action | Required |
| These are legacy services and known vulnerable to many types of denial of service attacks. | Under Control Panel, Services – Set service to DISABLED. | L | M | H |
| TCP/IP Print Server |
| Description | Action | Required |
| Service should be disabled if the server is not providing TCP print services/spooling. | Under Control Panel, Services – Set service to DISABLED. | L | M | H |
| QOS RSVP |
| Description | Action | Required |
| This service is not required by most systems and is used primarily as a routing performance service. | Under Control Panel, Services – Set service mode to DISABLED. | L | M | H |
| Clip Book |
| Description | Action | Required |
| Allows clip book views from a remote location to read clip book files on the server.. | Under Control Panel, Services – Set service mode to DISABLED. | L | M | H |
| Fax Service |
| Description | Action | Required |
| This service is often installed by third party products or as part of the 2K install. It should only be used in specific Fax and RAS configurations. | Under Control Panel, Services – Set service mode to DISABLED. | L | M | H |
| Indexing |
| Description | Action | Required |
| The Indexing service provides for fast file access by indexing file table entries. It has been exploited and should not be used unless needed. | Under Control Panel, Services – Set service mode to MANUAL or DISABLED. | L | M | H |
| Enabled Services List |
| Description | Action | Required |
| The following services are normally required for 2K to work properly and can be safely enabled. | Under Control Panel, Services – Automatic Updates DHCP Client (When on DHCP Network) DISTRIBUTED LINK Tracking Client DNS Client Event Log IPSEC Policy Agent Logical Disk Manager NetLogon Plug and Play Protected Storage Remote Procedure Call (DFS File Systems) Security Accounts Manager Server System Event Notification TCP/IP NetBios Helper Windows Time Workstation Note: Automatic Updates should only be used on servers configured to use a local Microsoft SUP server that receives updates after thorough testing. | L | M | H |
| Net Meeting Remote Desktop Sharing |
| Description | Action | Required |
| Net meeting allows remote computers to take control of your desktop. This service should be disabled unless absolutely needed. | Under Control Panel, Services – Set to Manual or DISABLED. | L | M | H |

# Registry Settings

The default permissions or access control lists applied to the registry are much more secure with 2K than they were with NT 4. The following implementation guidance secures the registry even tighter than the default install.

Each heading is followed by the applicable registry location, a description of why the action is necessary, and a description of the required registry changes.

Where registry keys do not already exist, they must be created.

| Resilience to Distributed Denial of Service Attacks |
| --- |
| HKLM\System\CurrentControlSet\Services\Tcpip\Parameters |
| Description | Action | Required |
| These settings should be added to the registry to make the system resilient to DDOS attacks. | Registry Value Entry Format Value EnableICMPRedirect DWORD 0 SynAttackProtect DWORD 2 EnableDeadGWDetect DWORD 0 EnablePMTUDiscovery DWORD 0 KeepAliveTime DWORD 300,000 DisableIPSourceRouting DWORD 2 TcpMaxConnectResponseRetransmissions DWORD 2 TcpMaxDataRetransmissions DWORD 3 PerformRouterDiscovery DWORD 0 TCPMaxPortsExhausted DWORD 5 | L | M | H |
| Handling Half-Open HTTP and FTP Requests |
| HKLM\System\CurrentControlSet\Services\AFD\Parameters |
| Description | Action | Required |
| Add these registry entries to allow afd.sys to better handle half-open HTTP and FTP requests through dynamic backlogging. | Registry Value Entry Format Value DynamicBacklogGrowthDelta DWORD 10 EnableDynamicBacklog DWORD 1 MinimumDynamicBacklog DWORD 20 MaximumDynamicBacklog DWORD 20000 | L | M | H |
| Protection Against Discovery of NetBIOS Name |
| WARNING! In some situations, this registry entry may cause WINS to stop working. This must be tested in advance of deployment. The NetBIOS names can also be loaded into the LMHOSTS file as an option to adding this registry key. |
| HKLM\System\CurrentControlSet\Services\Netbt\Parameters |
| Description | Action | Required |
| Add this value registry entry to stop attacks that make a computer release its NetBIOS name. This information is used by an attacker in NetBIOS discovery. | Registry Value Entry Format Value NoNameReleaseOnDemand DWORD 1 | L | M | H |
| Disable The Use of 8.3 File Name Conventions |
| HKLM\System\CurrentControlSet\Control\FileSystem |
| Description | Action | Required |
| Add this registry entry to disable the use of 8.3 file name conventions. Attackers could access long file names using short name standards. | Registry Value Entry Format Value NtfsDisable8dot3NameCreation DWORD 1 | L | M | H |
| Disable Autorun On CDROM Drives |
| HKLM\SOFTWARE\Microsoft\Windows\CurrentVersion\Policies\Explorer |
| Description | Action | Required |
| This registry entry will stop autorun on CDROM drives to prevent malicious code from running. | Registry Value Entry Format Value NoDriveTypeAutoRun DWORD 0xFF | L | M | H |
| Remove The OS2 And POSIX Subsystems |
| HKLM\SYSTEM\CurrentControlSet\Control\Session Manager\SubSystems |
| Description | Action | Required |
| This registry entry removes OS2 and POSIX subsystems. | Delete these subkeys: Optional OS/2 POSIX | L | M | H |
| Eliminate Screen Saver Grace Period |
| HKLM\SYSTEM\Software\Microsoft\WindowsNT\CurrentVersion\Winlogon \ScreenSaverGracePeriod |
| Description | Action | Required |
| This registry entry makes screen saver activity immediate with no grace period. | Registry Value Entry Format Value ScreenSaverGracePeriod String 0 | L | M | H |
| Protection of Kernel Object Attributes |
| HKLM\SYSTEM\CurrentControlSet\Control\Session Manager |
| Description | Action | Required |
| This setting ensures that the object manager may change attributes of a kernel object in the object table for the current process if, and only if, the previous mode of the caller is kernel mode. | Registry Value Entry Format Value EnhancedSecurityLevel DWORD 1 | L | M | H |
| Restrict Null Access to Shares |
| HKLM\SYSTEM\CurrentControlSet\Services\lanmanserver\parameters |
| Description | Action | Required |
| This registry entry restricts null access to shares on the computer. | Registry Value Entry Format Value RestrictNullSessAccess DWORD 1 DELETE NullSessionPipes DELETE NullSessionShares | L | M | H |
| Event Log 90% Full Warning |
| HKLM\SYSTEM\CurrentControlSet\Services\Eventlog\Security |
| Description | Action | Required |
| This registry entry gives a warning in the event log that log level is 90% full. | Registry Value Entry Format Value WarningLevel DWORD 90 | L | M | H |
| Bypass Cached Credentials Without Upgrading Privileges |
| HKLM\Software\Microsoft\Windows NT\CurrentVersion\Winlogon |
| Description | Action | Required |
| Add This registry entry to bypass cached credentials and allow locally locked out accounts to still access the domain without upgrading privileges. | Registry Value Entry Format Value ForceUnlockLogon DWORD 1 | L | M | H |
| Disable LM Hash Creation |
| WARNING! Have users change password after this key is added because LM Hash data is cached on the server. |
| HKLM\SYSTEM\CurrentControlSet\Control\Lsa\ |
| Description | Action | Required |
| Add This registry key to disables LM Hash creation. Tools such as L0phtcrack can pick LM Hashes from the network. | Registry Value Entry Format Value Add NoLMHash key to above entry | L | M | H |

# Configure IPSEC

Internet Protocol Security (IPSEC) was initially designed to encrypt data as it travels between two computers. IPSEC can also be used to lockdown the network interface by locking down ports. This is an excellent strategy to use to help protect against internal attacks, or to add security resilience to a compromised network.

IPSEC policies can be implemented in the IP Security Policies section of the Local Security Settings MMC snap-in. Included in the 2K Resource Kit is IPSecPol.exe. It is used to create, assign,  and delete IPSEC policies from the command line.

The syntax of IPSecPol.exe is:

Ipsecpol –w REG –p “Packet Filter” –r “Inbound Web” –f  *+hostIP:hostport:TCP –n pass

Where –w REG writes a static policy to the registry

Where –p creates a policy called Packet Filter

Where –r creates a rule called Inbound Web

Where –f adds the filter, *=any source address and any port, hostIP=IP addess of protected server, hostport=port to apply filter too

Where –n PASS allows traffic to pass.

| Add Packet Filters Using IPSEC |
| --- |
| Description | Action | Required |
| Administrators can easily script the execution of IPSEC filters to apply across the domain. Required ports should be allowed for server roles, like for Web Servers, Mail Servers, and DNS Servers. The follwing example is for a DNS Server. ONLY OPEN REQUIRED PORTS. | Ipsecpol –w REG –p “Packet Filter” –r “DNS” –f *+192.168.0.1:53:TCP –f *+192.168.0.1:53:UDP –n pass | L | M | H |
| Add Block All with IPSEC |
| Description | Action | Required |
| This IPSEC policy will block all that is not specifically allowed. | Ipsecpol –w REG –p “Packet Filter” –r “DENY Inbound” –f *+192.168.0.1 –n BLOCK | L | M | H |
| Assign IPSEC Policy |
| Description | Action | Required |
| This last command assigns the IPSEC policy. | Ipsecpol –w REG –p “Packet Filter” –r “DENY Inbound” –f *+192.168.0.1 –n BLOCK | L | M | H |
| Add Block All with IPSEC |
| Information! By replacing the –x flag with –o the policy can be deleted. The policy can be unassigned with the –y flag. |
| Description | Action | Required |
| This IPSEC policy will block all that is not specifically allowed. | Ipsecpol –w REG –p “Packet Filter” –x | L | M | H |

# Files and Permissions

| Move CMD.EXE |
| --- |
| Description | Action | Required |
| This file should be moved to a location that is not in the environment path and authorized access by only the Administrator. | Create a directory out of path called AAO (admin access only) and move c:\winnt\system32\cmd.exe to the AAO directory. | L | M | H |
| Move FINGER.EXE |
| Description | Action | Required |
| This file should be moved to a location that is not in the environment path and authorized access by only the Administrator. | Move finger.exe to the AAO directory. | L | M | H |
| Move NBTSTAT.EXE |
| Description | Action | Required |
| This file should be moved to a location that is not in the environment path and authorized access by only the Administrator | Move NBTSTAT.exe to the AAO directory. | L | M | H |
| Move NETSTAT.EXE |
| Description | Action | Required |
| This file should be moved to a location that is not in the environment path and authorized access by only the Administrator | Move netstat.exe to the AAO directory. | L | M | H |
| Move RSH.EXE |
| Description | Action | Required |
| This file should be moved to a location that is not in the environment path and authorized access by only the Administrator | Move the RSH.exe file to the AAO directory. | L | M | H |
| Move RCP.EXE |
| Description | Action | Required |
| This file should be moved to a location that is not in the environment path and authorized access by only the Administrator | Move the RCP.exe file to the AAO directory. | L | M | H |
| Move ROUTE.EXE |
| Description | Action | Required |
| This file should be moved to a location that is not in the environment path and authorized access by only the Administrator | Move the Route.exe file to the AAO directory. | L | M | H |
| Move TELNET.EXE |
| Description | Action | Required |
| This file should be moved to a location that is not in the environment path and authorized access by only the Administrator | Move the telnet.exe file to the AAO directory. | L | M | H |
| Move TFTP.EXE |
| Description | Action | Required |
| This file should be moved to a location that is not in the environment path and authorized access by only the Administrator | Move the tftp.exe file to the AAO directory. | L | M | H |
| Move TRACERT.EXE |
| Description | Action | Required |
| This file should be moved to a location that is not in the environment path and authorized access by only the Administrator | Move the TRACERT.exe file to the AAO directory. | L | M | H |
| Move COMMAND.COM |
| Description | Action | Required |
| This file should be moved to a location that is not in the environment path and authorized access by only the Administrator | Move the COMMAND.COM file to the AAO directory. | L | M | H |
| Remove DOS Files |
| Description | Action | Required |
| This directory should be removed to prevent an attacker from booting to the DOS Kernel. | Search for a directory called DOS. If found, Delete the Directory. | L | M | H |
| Remove OS/2 Subsystem Files |
| Description | Action | Required |
| These files should be removed. | Search for and delete the following files and directories: OS2 (DIR) Os2.exe Os2srv.exe Os2ss.exe Netapi.os2 | L | M | H |
| Remove POSIX Subsystem |
| Description | Action | Required |
| These files should be removed. | Search for and delete the following files or directories: Posix.exe Psxdll.dll Psxss.exe | L | M | H |
| Move NET.EXE |
| Description | Action | Required |
| This file should be moved to a location that is not in the environment path and authorized access by only the Administrator | Move the Net.exe file to the AAO directory. | L | M | H |
| Move IPCONFIG.EXE |
| Description | Action | Required |
| This file should be moved to a location that is not in the environment path and authorized access by only the Administrator | Move the IPConfig.exe file to the AAO directory. | L | M | H |
| Move PING.EXE |
| Description | Action | Required |
| This file should be moved to a location that is not in the environment path and authorized access by only the Administrator | Move the Ping.exe file to the AAO directory. | L | M | H |
| Move REGEDT32.EXE |
| Description | Action | Required |
| This file should be moved to a location that is not in the environment path and authorized access by only the Administrator | Move the RegEdt32.exe file to the AAO directory. | L | M | H |

Note: Some of the files listed in the following table may have been moved in the previous section.  Their new location should be used instead of the \Winnt\System32 directory named below.

| Change File Permissions All Risk Categories L M H |
| --- |
| FILE /DIRECTORY | USER/GROUP | PERMISSIONS |
| C:\ (Propagate instead of Replace) | Administrators CREATOR OWNER SYSTEM Users | Full Control Full Control (subfolders and files) Full Control Traverse folder, Read attributes, Read extended attributes, Create files, Create folders (folder and subfolders) |
| C:\autoexec.bat | Administrators SYSTEM Users | Full Control Full Control Read, Execute |
| C:\boot.ini | Administrators SYSTEM | Full Control Full Control |
| C:\config.sys | Administrators SYSTEM Users | Full Control Full Control Read, Execute |
| C:\Documents and Settings (Propagate instead of Replace) | Administrators SYSTEM Users | Full Control Full Control Read, Execute |
| C:\Documents and Settings\All Users (Propagate instead of Replace) | Administrators SYSTEM Users | Full Control Full Control Read, Execute |
| C:\Documents and Settings\Default User | Administrators SYSTEM Users | Full Control Full Control Read, Execute |
| C:\io.sys | Administrators SYSTEM Users | Full Control Full Control Read, Execute |
| C:\msdos.sys | Administrators SYSTEM Users | Full Control Full Control Read, Execute |
| C:\ntdetect.com | Administrators SYSTEM | Full Control Full Control |
| C:\ntldr | Administrators SYSTEM | Full Control Full Control |
| C:\Program Files | Administrators CREATOR OWNER SYSTEM Users | Full Control Full Control (subfolders and files) Full Control Read, Execute |
| %SystemRoot% (C:\Winnt by default) | Administrators CREATOR OWNER SYSTEM Users | Full Control Full Control (subfolders and files) Full Control Read, Execute |
| %SystemRoot%\$NtServicePackUninstall$ | Administrators SYSTEM | Full Control Full Control |
| %SystemRoot%\debug (Propagate instead of Replace) | Administrators CREATOR OWNER SYSTEM Users | Full Control Full Control (subfolders and files) Full Control Read, Execute |
| %SystemRoot%\NTDS (May not be in %SystemRoot%, check to make sure) (Propagate instead of Replace) | Administrators SYSTEM | Full Control Full Control |
| %SystemRoot%\regedit.exe | Administrators SYSTEM | Full Control Full Control |
| %SystemRoot%\Repair | Administrators SYSTEM | Full Control Full Control |
| %SystemRoot%\System32 | Administrators CREATOR OWNER SYSTEM Users | Full Control Full Control (subfolders and files) Full Control Read, Execute |
| %SystemRoot%\System32\config | Administrators SYSTEM | Full Control Full Control |
| %SystemRoot%\System32\dllcache | Administrators CREATOR OWNER SYSTEM | Full Control Full Control Full Control |
| %SystemRoot%\System32\GroupPolicy (Propagate instead of Replace) | Administrators Authenticated Users SYSTEM | Full Control Read, Execute Full Control |
| %SystemRoot%\System32\ias | Administrators CREATOR OWNER SYSTEM | Full Control Full Control Full Control |
| %SystemRoot%\System32\Ntbackup.exe | Administrators SYSTEM | Full Control Full Control |
| %SystemRoot%\System32\Regedt32.exe | Administrators SYSTEM | Full Control Full Control |
| %SystemRoot%\System32\secedit.exe | Administrators SYSTEM | Full Control Full Control |

# USER RIGHTS POLICY CONFIGURATION

These configurations are intended for moderate to high risk computer systems. This is especially true for systems containing sensitive or classified information.

| User Rights M H |
| --- |
|  | Authorized Groups |
| Users Rights | Domain Controllers | Member Servers | 2K Professional |
| Access this computer from network | Administrators Authenticated Users Enterprise Domain Controllers | Administrators Users | Administrators Users |
| Act as part of the operating system * | (None) | (None) | (None) |
| Add workstations to domain | Administrators Enterprise Domain Admins | Administrators | Administrators |
| Backup files and directories* | Administrators Backup Operators | Administrators Backup Operators | Administrators Backup Operators |
| Bypass traverse checking* | Authenticated Users | Users | Users |
| Change the system time | Administrators Server Operators | Administrators Server Operators | Administrators Server Operators |
| Create a pagefile | Administrators | Administrators | Administrators |
| Create a token object | (None) | (None) | (None) |
| Create permanent shared objects | (None) | (None) | (None) |
| Debug programs | (None) | (None) | (None) |
| Deny access to this computer from the network | Guests | Guests | Guests |
| Deny logon as a batch job | (None) | (None) | (None) |
| Deny logon as a service | (None) | (None) | (None) |
| Deny logon locally | Guests | Guests | Guests |
| Enable computer and user accounts to be trusted for delegation | Administrators | (None) | (None) |
| Force shutdown from a remote system | Administrators Enterprise Domain Admins Server Operators | Administrators Enterprise Domain Admins Server Operators | Administrators Enterprise Domain Admins Server Operators |
| Generate security audits | (None) | (None) | (None) |
| Increase quotas | Administrators | Administrators | Administrators |
| Increase scheduling priority | Administrators | Administrators | Administrators |
| Load and unload device drivers | Administrators | Administrators | Administrators |
| Lock pages in memory | (None) | (None) | (None) |
| Log on as a batch job | (None) | (None) | (None) |
| Log on as a service * | (None) | (None) | (None) |
| Log on locally * | Administrators Backup Operators | Administrators Backup Operators | Administrators Users |
| Manage auditing and security log* | Auditor’s Group (Exchange Enterprise Servers Group) | Auditor’s Group (Exchange Enterprise Servers Group on Exchange server) | Auditor’s Group |
| Modify firmware environment values | Administrators | Administrators | Administrators |
| Profile single process | Administrators | Administrators | Administrators |
| Profile system performance | Administrators | Administrators | Administrators |
| Remove computer from docking station | (None) | (None) | Administrators Users |
| Replace a process level token | (None) | (None) | (None) |
| Restore files and directories* | Administrators Backup Operators | Administrators Backup Operators | Administrators Backup Operators |
| Shut down the system | Administrators | Administrators | Administrators Users |
| Synchronize directory service data | (None) | (None) | (None) |
| Take ownership of files or other objects | Administrators | Administrators | Administrators |

# GENERAL SECURITY

| Install Antivirus |
| --- |
| Description | Action | Required |
| Anti-virus software should be installed on all systems. | Install anti-virus software and insure the update policy is daily. Up-to-date anti-virus definitions and signatures can be burned to a CD and installed before the system is connected to the network. | L | M | H |
| Create NTFS Volumes And Disks |
| Description | Action | Required |
| NTFS file systems provide a way of controlling file access and enable permissions and ACL’s to be placed on specific files and folders. | Remove FAT volumes and Drives and either format or convert them to NTFS. | L | M | H |
| Windows Update |
| Description | Action | Required |
| This program should be installed on all desktop computers. | Low risk computers (like desktops) should have Windows Update set to retrieve and install files. Moderate risk computers should have Windows Update retrieve files and prompt for installation of patches, service packs, and hot fixes. High risk computers should have hotfixes and patches installed manually within 2 hours of the release of the hot fix or security patch. | L | M | H |
| Do Not Allow Automatic Logons |
| Description | Action | Required |
| Automatic logons are a convenience function built into 2K. This should not be allowed. | Ensure Security Options are not set to allow automatic logon for the administrator. | L | M | H |
| Install Dummy Administrator Account |
| Description | Action | Required |
| A dummy administrator account can be created with no privileges to track attacks against a system. | Only required if policy dictates. Create an Administrator Account and allow NO privileges. | L | M | H |
| Remove Power Users |
| Description | Action | Required |
| Power User group should have no members. There is no need in a Forest or Domain structure to include power users. | Remove all users from the Power Users Group. | L | M | H |
| Remove Local Accounts From Domain Member Wks |
| Description | Action | Required |
| Workstations on a Domain should not have local user accounts. | Remove all users except the local Administrator user from workstations participating in a domain. | L | M | H |
| Remove Default Shares From Workstations |
| WARNING! This may cause some applications and services to stop working. |
| Description | Action | Required |
| 2K opens hidden shares that should be disabled. | DISABLE the SERVER SERVICE | L | M | H |
| Remove Modems From Workstations |
| Description | Action | Required |
| Modems are an easy way to access a system or bypass network security features. Remove all modems, unless absolutely required, from all workstations in the Domain. | Remove all modems Except from protected RAS servers. | L | M | H |
| Replace Everyone Group With Auth Users |
| Description | Action | Required |
| Domain shares are necessary but should not include access by the everyone group. | On domain shares, replace the everyone group with the authenticated users group. | L | M | H |
| Create Security Group – Set Permissions On Logs |
| Description | Action | Required |
| The logs should only be readable by a member of the security group.. | Create a security group and change permissions on the security event log so that only ISSO’s can read the logs. | L | M | H |
| Enable Startup Password |
| Description | Action | Required |
| A Startup password will prevent users from using password changing utilities to change the Administrators password. | Create a startup password. Consult the users manual for access to the system bios. | L | M | H |
| Install Service Applications Off The Root Drive |
| Description | Action | Required |
| Services like DNS, HTTP, and Mail (various), should be installed off the system root drive and onto a separate drive or volume. | Set web root or DNS zone files on a separate drive or volume than the system root.. | L | M | H |

# Footnotes

From The DoD Field Security Operations Guide for Windows 2000, Chapter 5