Nokia / Checkpoint Initial Setup

This document describes the step-by-step procedures for installing IPSO on an IPxxx, and installing / setting up Checkpoint FWx Module.

| Initial Installation – through a console session: Console Settings : 9600, 8,N,1,N (not needed if keeping current IPSO and Checkpoint Rev. Go to Section2) |
| --- |
| Step | Description | Procedure | Comments |
|  | As appliance is booting , it will prompt you to “Hit any key to enter command mode”. Be quick, it only gives you a second. | Bootmgr > Install Continue? Y |  |
|  |  | Enter: FW serial number | Located on base of firewall unit |
|  |  | Choose product - #4 |  |
|  |  | IGRP? N |  |
|  |  | BGP? N |  |
| Install from Anonymous FTP Server (#1) (Note : Use PC that is being used to configure system) |
|  |  | IP Address of client IP Address of FTP Server IP address of gateway |  |
|  |  | Path to the IPSO and CP packages you wish to load (for example: ./nokia/nokiaipso3.4, or C:\Inetpub\ftproot for WNT this directory should contain both IPSO3.x and CP4.1) packages |  |
|  |  | Retrieve ALL packages (#1) |  |
|  |  | Verify Information is correct? Y |  |
|  | IPSO loads at this point |  |  |
|  | Load verifies |  |  |
| REBOOT |  |  |  |

| Initial appliance setup |
| --- |
| Step | Description | Procedure | Comments |
|  | Enter Hostname | Type in host name of the box |  |
|  | <hostname> okay? Y | Confirm Name. |  |
|  | Enter password | Select alphanumeric |  |
|  | Confirm password |  |  |
|  | Configure system with web based VOYAGER | Select Option 1 |  |
|  | Select Interface to be configured | ETH-S1P1 | Internal interface |
|  | Interface IP address (note: if configuring at ACME, make sure a ACME address is used) | Enter IP address | Put 10.x.x.x/16 if you want to skip next question. |
|  | Interface Mask Length | Put number of bits (16) |  |
|  | Set default route | Enter default route | Acme is 10.1.1.254 |
|  | Interface speed – 100Mb |  |  |
|  | Interface mode – Full Duplex |  |  |
| Loads Packages (only prompted if doing Section #1) |
|  | FW1 Strong Documentation Open Services (optional) | Install as new package | Install all as new packages to clean system |
| REBOOT |
| Go to “Voyager” for the rest of the configuration setup: http://ip-adddress-for ETH-S1P1 The other Ethernet interfaces will be setup later in Voyager. |

| Open a Web Browser, and put address of firewall: http://ip-adddress-for ETH-S1P1 The other Ethernet interfaces will be setup later in Voyager. |
| --- |
| Step | Description | Procedure | Comments |
| Select “Config” button from “home” menu |  | From the Config options, SCROLL down to…. |  |
| Security and Access Configuration | Select “Network Access & Services” | TELNET = OFF Apply Save Up |  |
|  | Select Checkpoint FW-1 | #1 – ON #2 – OFF #3 – OFF Apply Save |  |
|  | Select SSH | Enable SSH service – Yes Admin user – Yes Retain all default values |  |
|  | Generate Encryption Keys | Generate New Key Select 1024 for RSA Select 1024 for DSA Apply Save Up |  |
| System Configuration | Select DNS | Enter domain name Apply Enter Primary Server Address Apply Save Up |  |
|  | Select Mail | Enter mail Server IP address Enter Remote User Email address (fwadmin@.....) Apply Save Up |  |
|  | Select System Failure Notification | Enable – ON Enter Email Address ( fwadmin@.....) Apply Save Up |  |

| Step | Description | Procedures | Comments |
| --- | --- | --- | --- |
|  | Select Local Time Setup | Select Timezone Set Date & Time Apply Save Up |  |
|  | Select Host Address Assignment | Enter FW name Apply Enter FW IP Address Apply Save Up |  |
|  | Manage Installed Packages | Turn ON Checkpoint FW-1 Documentation Apply Save Up |  |
| Set up Interface Configuration | Interfaces S2P1 | Select Logical name (ETH-S1P1) AND Change to “Internal” Apply Save Up Change IF#2 logical name to “External” Apply Save Up |  |
|  | Select Physical IF#2 | PhysicalActive – ON 100Mb Full Duplex Logical Active – ON Apply Save UP |  |
| Router Services | Select NTP | Enable – Yes Apply Add NTP server Addresses Apply Save Up |  |
| REBOOT |

| Initial Installation – through a console session: Console Settings : 9600, 8,N,1,N Initial Checkpoint Configuration - from console |
| --- |
| Step | Description | Procedure | Comments |
| Enter Checkpoint configuration | At prompt, type cpconfig |  |  |
|  | Accept License – Yes | Type “q” to bypass text |  |
|  | Choosing Installation | Select 1 if stand alone Select 2 if High Availability System |  |
|  | Module | Select the appropriate option for the licenses |  |
|  | Add licenses | No. Add licenses later |  |
|  | Add Administrators | fwadmin, appropriate user(s) Set/remember the password and allow for read/write access (W) |  |
|  | Add GUI clients – Yes | Add IP address for each client Enter CNTL-D on blank line Type Yes if addresses are correct |  |
|  | Name the external interface | Type external |  |
|  | SMTP Server | Take all defaults until: Postmaster – fwadmin@..... Default Server - <enter mail server IP address> |  |
|  | SNMP – NO |  |  |
|  | Set Up Groups | Enter for No Groups Confirm? Yes |  |
|  | Generate Secret Keys | Type characters until appliance beeps |  |
|  | Start FW on reboot? | NO |  |
| REBOOT |
| When appliance comes back up, at console prompt type fwstop Note: fwstart (won’t work until you have added licenses) |
| Now you can connect to Voyager and through Voyager you can setup VRRP, routes in the other 7 interfaces etc…. This is done using IE6/Netscape: http://ip-addr-of the-box: |

| Setting up a secure access the Nokia through Voyager Initial Connection is done with IE6 (128) bit encryption: http://ip-addr-of the-box |
| --- |
| Step | Description | Procedure | Comments |
| Launch IE6 or Netscape | Accessing Voyager | http://ip-addr-of the-box |  |
| Select Certificate | We are going to generate a x509 cert | Select Certificate Tool |  |
|  |  | Select 1024 bits |  |
|  |  | Enter passphrase and verification |  |
|  |  | Fill in the fields, the bolded fields are required |  |
|  |  | Select Self-signed x509 Certificate |  |
|  |  | APPLY |  |
| Using Voyager/ssl | This must be done 1st | Select Voyager Access | 1st Step |
|  |  | Scroll down to Configure SSL Certificate |  |
|  |  | Cut and paste the Certificate and private key in the boxes then enter the passphrase |  |
|  |  | You will receive a confirmation that it accepted the certificate. When you enter the certificate and private key you need to cut/paste the whole text including the Begin and End lines |  |
|  | Then do this 2nd |  | 2nd Step |
|  |  | Select require encryption |  |
|  |  | Select 128 bit or stronger |  |
|  |  | Apply |  |
|  |  | Save |  |
| Now you will be disconnected in IE6/Netscape; you need to reconnect using: https://ip-addr-of the-box:443 – SSL Connection to Voyager. Note: SSL will use port 443, this can be changed on the IP440, but is not recommended. |

Obtain the license from Checkpoint and save it to a .lic file, in a hyper-terminal session consoled into the Nokia box, add the license:

fw putlic file.lic

Review response for errors/messages.

Change the name of the alias that is generating mail messages:

dbset passwd:admin:realname FW1 / FW2

dbset :save

confgen

All email originating from the system will have as the sender " FW1 / FW2".  Use only alphanumeric characters and no spaces to set this option.

Definition of Firewall can now be started.

FYI:

Install folder on the Checkpoint FW cdrom

Solaris:

installU	D:\solaris2\CPfw1-41

GUI		D:\solaris2\CPgui-41

Windows NT:

Install file	D:\windows\CPFirewall1-41

GUI		D:\windows\CPMgmtClnt-41

Redhat:	D:\linux\CPfw1-41

RPM Install	D:\linux\CPsmc-41