Nokia Outline

Details:

Not an open system

BSD modified OS

Checkpoint firewall

Limited network support (no TR, FDDI, 100/10 base T)

No OPSEC support

Always a rev behind

Internet Protocol Security Option

Status lights - green online, yellow = active

Console db9 to rj11 (9600, 8, none, hardware none)

Voyager – (http:80) - IPSO (NAP) – talks to OS/hardware

Ethernet description - eth or [ser] –s (slot) p [ports] {c0} for card number

3 ethernet ports (10/100)

Boot manager = defaults after 5 seconds

You can manage IPSO and update the Boot Manager

- sysinfo

- Prinenv

- Set defaults

- Install <ip address/Password>   “ftp access”

IP330 uses IPSO  proprietary Linux Kernal  (Network Access Protocol) NAP

AMD K6 Dual processor  <TAB> enters Bios

# IP330 Version Numbers

Build Number Service Pack

3083 3.0b SP8

3096 3.0b SP9

4031 4.0 SP1

4034 4.0 SP2

4056 4.0 SP3

4064 4.0 SP3 + hotfix

4066 4.0 SP4

4094 4.0 SP5

41439 4.1 SP0

41489 4.1 SP1

nokia[admin]# tput clear

nokia[admin]# while true

nokia[admin]# do

nokia[admin]# tput home

nokia[admin]# date

nokia[admin]# fw tab -t connections | grep

nokia[admin]# done

fw tab -t IKE_SA_table -x

yes

fw tab -t outbound_SPI -x

yes

fw tab -t ISAKMP_ESP_table -x

yes

fw tab -t inbound_SPI -x

yes