How to Recover a Lost or Forgotten Password

for "root" on a Sun/Solaris System

## Introduction

If you forget your root password on the Sun Solaris Platform, the following procedure erases your current password and allows you to specify a new one. All other configurations will remain the same.

#### Hardware and Software Versions

This is applicable on SUN Solaris 2.x / SunOS 5.x platforms. You will need a cdrom drive and a Solaris installation cdrom. Make sure the installation cdrom is equal to, or later than, the OS release on the hard disk.

#### Step By Step Procedure

If the system is not halted, then halt the system by pressing Stop-A. This will bring you to the ok prompt.

- Place the installation cdrom in the cdrom drive. Boot the system to single user mode using the cdrom drive. Type: boot cdrom -s

- It may take a while but you will automatically be logged in as root in single user mode running the OS from the cdrom.

- If you had to force halt the system, by pressing Stop-A for instance, then the partitions on the hard disk will not be marked as being shutdown cleanly. If this happens, run fsck on the root partition. It is used to check and repair the file system. In this case it won't ask for the root password as it is in single user mode. Type: fsck -y /dev/dsk/c0t3d0s0

- Now c0t3d0s0 is just the root partition in this example. Verify your boot disk.

- Mount the root partition. The cdrom has created a directory a for mounting hard disks. Type: mount /dev/dsk/c0t3d0s0 /a

- Remove root's password using your editor, edit /a/etc/shadow.  Find root's entry in the file and make the second field null. Colons are the field delimeters. So your entry, after changes, should look something like:

    - root::10565::::::

- Various fields will be used if certain parameters have been set for the OS.

Boot to single user mode using the hard disk. Type: reboot -- -s

Note: That is reboot space hyphen hyphen space hyphen s.

- You can log in as root without a password and set root's password using the passwd command.

Exit single user mode and let the system continue booting to multi-user mode.