## Slide 1: FirePOWER
Kaustubh Vajarkar
Cisco FirePOWER TAC Engineer
Replacing your ASA/FTD with Firepower services

## Slide 2: STEPS
Collect important information from existing device
Download installer files for required version
Re-image new device to the required version
Restore configuration
Re-host licenses
Replace device

## Slide 3: Collect important information from existing device Download installer files for required version Re-image new device to the required version Restore configuration Re-host licenses Replace device
Collect version information
  show module
  show version
  show asdm image
Collect ASA license information
    show activation-key detail
    Configuration > ASA FirePOWER Configuration > Licenses and clicking Add New License. (To locate old license key if on-box managed)
  Create backup from ASDM
    ASA configuration backup
      http://www.cisco.com/c/en/us/td/docs/security/asa/asa83/asdm63/configuration_guide/config/admin_swconfig.html#wp1243681

## Slide 4: Collect important information from existing device Download installer files for required version Re-image new device to the required version Restore configuration Re-host licenses Replace device
Collect version information
  show version
FTD license information
    The FTD uses smart license and a token will be required to be downloaded from Cisco Smart Software Manager
  Create backup from FTD
    Firepower configuration backup if using on-box management
      http://www.cisco.com/c/en/us/support/docs/security/asa-5500-x-firepower-services/200448-Configure-Backup-Restore-of-Configurati.html

## Slide 5: Collect important information from existing device Download installer files for required version Re-image new device to the required version Restore configuration Re-host licenses Replace device
Device cabling

## Slide 6: Collect important information from existing device Download installer files for required version Re-image new device to the required version Restore configuration Re-host licenses Replace device
Download link
  http://www.cisco.com/go/asa-firepower-sw
Compatibility matrix
  http://www.cisco.com/c/en/us/td/docs/security/asa/compatibility/asamatrx.html
ASA
  asa953-lfbff-k8.SPA
ASDM
  asdm-771.bin
FirePOWER Boot Image
  asasfr-5500x-boot-6.1.0-330.img
Firepower Package Installer
  asasfr-sys-6.1.0-330.pkg
FTD boot image
  ftd-boot-9.6.2.0.lfbff
System software install package
  ftd-6.1.0-330.pkg

## Slide 7: Collect important information from existing device Download installer files for required version Re-image new device to the required version Restore configuration Re-host licenses Replace device
Install and Configure a FirePOWER Services Module on an ASA Platform
  http://www.cisco.com/c/en/us/support/docs/security/asa-firepower-services/118644-configure-firepower-00.html
Reimage the Cisco ASA or Firepower Threat Defense Device
  http://www.cisco.com/c/en/us/td/docs/security/firepower/quick_start/reimage/asa-ftd-reimage.html

## Slide 8: Collect important information from existing device Download installer files for required version Re-image new device to the required version Restore configuration Re-host licenses Replace device
Install basic configuration on ASA and connect via ASDM
  Cisco ASA 5506-X Series Quick Start Guide
    http://www.cisco.com/c/en/us/td/docs/security/asa/quick_start/5506X/5506x-quick-start.html
  Cisco ASA 5508-X and ASA 5516-X Quick Start Guide
    http://www.cisco.com/c/en/us/td/docs/security/asa/quick_start/5508X/5508x-quick-start.html
Restore backup for ASA using ASDM
  Restoring Configurations
    http://www.cisco.com/c/en/us/td/docs/security/asa/asa83/asdm63/configuration_guide/config/admin_swconfig.html#wp1244402
Restore Firepower module if on-box managed
Provision network settings to Firepower module
  ciscoasa# session sfr console
  > configure network ipv4 manual ipaddr netmask gw

## Slide 9: Collect important information from existing device Download installer files for required version Re-image new device to the required version Restore configuration Re-host licenses Replace device
Assign management IP address on the new FTD
Restore the previously taken backup

## Slide 10: Collect important information from existing device Download installer files for required version Re-image new device to the required version Restore configuration Re-host licenses Replace device
Product License Registration
  http://www.cisco.com/go/license
FTD uses smart licenses and a token will be required to be downloaded from Cisco Smart Software Manager

## Slide 11: Collect important information from existing device Download installer files for required version Re-image new device to the required version Restore configuration Re-host licenses Replace device
Connect cables according to the network diagram
Delete old FirePOWER module/FTD from FirePOWER Management Center GUI
  Device > Device management > Delete device.
Add the FirePOWER module/FTD in the new device to the Management Center
  > configure manager add fmcIP regkey
Deploy policies to the device
Verify connection events indicating correct functionality of the FirePOWER module.

## Slide 12: FirePOWER Kaustubh Vajarkar Cisco FirePOWER TAC Engineer
THANK YOU